## Slide 1: Requirements for Personnel, Services, Equipment and Sources
Lecture 1.8

## Slide 2
Personnel…
The installation must keep the following data from all occupationally exposed workers:
Names and surnames
Qualification
Training
Psycho-physical fitness

## Slide 3
Personnel requirements:
The staff must have at least:
  Radiation Protection Officer and physicians;
  Physician / s in nuclear medicine;
  Qualified experts in nuclear medicine physics;
  Technologists in nuclear medicine;
  Qualified nursing staff.

## Slide 4
Personnel requirements:
The number and qualifications of the personnel involved must be adequately related to the postulated workload.
The facility must have available the documentation that staff qualifications and medical fitness are accredited by competent bodies recognized by the regulatory authority.

## Slide 5
Equipment:
A PET facility must have at least:
Activimeter;
Area monitors and contamination monitors;
Personal protective equipment;
Phantoms for quality control of PET camera.

## Slide 6
Equipment…
Activimeter: Equipment for calibration of the activity delivered to the patient.

## Slide 7
Equipment…
Activimeter:
Well-type chamber:
Sensitive to geometry;
Sensitive to energy;
Adjustable.

## Slide 8
Equipment…
Activimeter:
The calibration must be done at the factory, with traceable sources in relation to a standard laboratory.

## Slide 9
Equipment…
Activimeter:
Remote injection system

## Slide 10
Equipment…
personal protective equipment
Appropriate clothing should include, at a minimum, the lab coat and gloves.

## Slide 11
Equipment…
personal protective equipment
  Long tongs for the manipulation of the sources
  Shielded syringes

## Slide 12
Equipment…
Radiological surveillance instruments
Contamination meters for purposes of detecting contamination
Dose rate meters

## Slide 13
Equipment…
Radiological surveillance instruments
Contamination (PET)
  Proportional counters
  NaI (Tl) scintillation detector
Dose rate meters
  Tube - GM
  Ionization chamber
  Scintillation detector

## Slide 14
Equipment…
Phantoms for quality control of PET camera
They can be dedicated systems;

## Slide 15
Services…
The installation must have an individual monitoring program which must include the contracting of individual dosimetry service for all established occupational workers;
  The practice must be specified by the service provider;
  Dosimetry should consider the type of worker´s activity.

## Slide 16
Services…
The installation must have a program of quality control of its instrumentation that includes the contracting of calibration service of the area monitors and surface contamination;
  The calibration laboratories must be duly certified by the competent authority.

## Slide 17
Sources…
The installation must have sealed sources for the quality control of the activimeter and the PET cameras
Long half life
Approximate energy range
Range of activities
Calibrated with variation of 5%
Co57, Ba133, Cs137, Co60, Ge-68

## Slide 18
Sources…
The installation must maintain the inventory of radiation sources with the characteristics of each of them.

## Slide 19
For sealed calibration sources:
  Radionuclide;
  Activity
  Reference date
  Series No.
  Model
  No. Equipment or container series if associated
  Manufacturer
  Source category
  Use to be given and location

## Slide 20
For unsealed sources:
Radionuclide / radiopharmaceutical
Maximum activity
Physical / chemical form
Use to be given and location

## Slide 21
For radiation generating equipment:
  Type of equipment
  Model
  Year of manufacture
  No equipment and panel series
  type of radiation that emits
  Maximum power (Maximum voltage, Maximum current intensity)
  Manufacturer
  Supplier
  Use to be given and location

## Slide 22
The declared sources, their characteristics and activities must be related to the expected workload.
All source activities must be provided in the IS units and accompanied by the date on which the activity was determined.