## Slide 1
SAFETY ASSESSMENT

## Slide 2
Safety Assessment
... means to assess compliance with safety requirements (and thus the application of fundamental safety principles) with respect to all facilities and activities and in order to determine the measures to be taken to ensure safety.
How to apply it in the licensing?

## Slide 3
Safety Assessment
The safety assessment of the practice should cover the following aspects:
Identification of the initiating events of postulated accidents. Including:
  all human errors;

## Slide 4
Safety Assessment
Identification of the initiating events of probable accidents. Including:
  equipment failures;
  external events or the combination of them;

## Slide 5
Safety Assessment
In addition…
Description, for each initiating event, of existing safety barriers to prevent or mitigate accidents.

## Slide 6
Safety Assessment
Further…
The identification of initiating events may be carried out using standard hazard identification methods such as:
  Analysis of Failure Modes and Effects (FMEA);
  Hazard Analysis and Operability (HAZOP);
  Preliminary Hazard Analysis;
  Criteria of experts and others.

## Slide 7
Safety Assessment
In addition…
  As well as if the lessons learned from incidental and incidental situations have been taken into consideration;

## Slide 8
Safety Assssment
Further…
In the description of the severity of the potential consequences associated with each accident initiating event, the consequences must be specified to:
  workers;
  members of the public;
  patients
according to the potential effect that each accident initiating event could cause without taking into account the expected safety barriers or measures;

## Slide 9
Safety Assssment
Also…
The barriers and measures necessary to control the danger can be of three types:
  safety interlocks;
  alarms or safety warnings;
  safety and emergency procedures;

## Slide 10
Safety Assssment
Further…
The risks associated with each accident initiating event will depend on:
  the frequency of occurrence of the initiating event;
  the robustness of safety barriers;
  the severity of the potential consequences associated with each initiating event.

## Slide 11
Safety Assssment
Further…
Procedures should be established for periodic review of the safety assessment at intervals required by the regulatory body;

## Slide 12
Safety Assssment
Further…
The evaluation must identify the personnel subject to the highest exposures (highest doses). Typically the one whose tasks involve the fractioning and manipulation of radioactive material and the care of patients, that is, the medical specialists, the nuclear medicine technicians and the nursing staff.