## Slide 1
Radioactive waste management and discharges to the environment

## Slide 2
Summary
Classification and Characterization of Radioactive Waste
Management of Disused Sealed Sources
Conditioning
Storage
Recycling and Reuse
Discharges
Records and Reports in the Management of Radioactive Waste
Protection and Physical Security

## Slide 3: Classification and Characterization of Radioactive Waste
Radioactive waste must be classified according to the national classification scheme that must take into account:
half-life period;
activity content by radionuclide;
physical and chemical form;
spent sealed or disused sources;
waste characterized by non-radiological risks (for example, chemical and biological toxicity).

## Slide 4: Management of Disused Sealed Sources
Procedures must be established that take into account all the possible variants for the future management of the disused sealed sources, such as:
a) return to the manufacturer or supplier, as a preferred solution;
b) transfer to any other authorized organization, when the source complies with the requirements for its safe use;

## Slide 5: Management of Disused Sealed Sources
c) temporarily store in the installation itself until the management path is defined;
d) transfer to an authorized facility for temporary or prolonged storage as radioactive waste.

## Slide 6: Conditioning
The conditioning must be compatible with the selected materials and processes and the acceptance criteria;
Waste packages must be designed and produced in such a way that the radionuclides remain confined;

## Slide 7: Conditioning
The information should include at least for each package:
Identification number of the package;
Type and details of package design;
Weight of the package;
External size and / or volume of the package;
Maximum dose rate in contact and at 1 m and the date of measurement;
Results of the surface contamination measurement;
Radionuclide content and activity concentration;
Potential presence of chemical, biological or other hazards.

## Slide 8: Conditioning
Example of the information that should be associated with the package.

## Slide 9: Storage
Radioactive waste containing radionuclides only very short periods of half-life, may be stored in the generating facility until the activity is below clearance levels, allowing the dispensed wastes are managed as conventional waste. Hence the importance of clearance levels or authorized discharges and verify that option in the application filed;

## Slide 10: Storage
The waste must be stored in a way that ensures:
a) the separation of treated and conditioned radioactive wastes from unconditioned wastes, non-radioactive materials and maintenance equipment;
Example of unsuitable storage

## Slide 11: Storage
The waste must be stored in a way that ensures:
b) that the allocation of a separate storage area, where radioactive biomedical waste is produced in large volumes, be considered.

## Slide 12: Storage
For the design and construction of the store should consider the following:
a) the conditions assumed for its normal operation and possible incidents or accidents;
b) planned or expected storage period;

## Slide 13: Storage
For the design and construction of the store should consider the following:
c) the potential use of passive safety measures, considering their potential degradation;
d) that the waste be inspected, monitored, recovered and kept in suitable conditions for its release.

## Slide 14: Discharges
The applicant must implement procedures to ensure that no radioactive materials from authorized practices to the environment unless downloaded:
1. such discharge is within the limits specified in the license and is performed in a controlled manner in accordance with the regulations in force and with the authorization issued by the regulatory body; or
2. it has been confirmed that the activity to be discharged is below the levels established by the regulatory body.

## Slide 15: Discharges
The applicant must possess detailed procedures for determining the characteristics and activity of the material to be discharged, and the potential points and methods of discharge, such as:
the composition of the radionuclide,
chemical and physical form of radionuclides, particularly if this is important for behavior in the environment

## Slide 16: Discharges
Further…
discharges routes and points of discharge,
the total amount of radionuclides expected to be discharged each year,
the expected time model for downloads;

## Slide 17: Discharges
Example of storage time calculation
"... The same hypothesis will be used for the calculation of the fluorine (F-18), that is, that 1/6 (333.33 mCi) of the weekly activity is not used or that the volume to be stored is the same two isotopes previously calculated, that is, 1ml. So we have to:
* F – 18
C0 = 333,33 mCi/ml,
Regulatory limit for discharge: C = 2x10-2μCi/ml,
T½ = 6 hours
C = C0.e-λt → t = 16,629 /0,3787
→ t = 43,9 hours o t ≈ 45 hours
...”

## Slide 18: Records and reports on the management of radioactive waste
Records related to the activities of the management and inventory of radioactive waste, including disused sources, shall:
a) stay updated;
b) retained in a way that ensures that all important information is always available;
c) guarantee the traceability of the waste from the moment of its generation and collection to temporary storage or its final disposal;

## Slide 19: Records and reports on the management of radioactive waste
The records related to the characteristics of the waste must contain, at least, the following information:
a) data from the source of origin;
b) the physical and chemical form;
c) the quantity (volume and / or mass);
d) the radiological characteristics (the concentration of activity, the total activity, the radionuclides present and their relative proportions);
e) classification in accordance with the national classification scheme for radioactive waste;

## Slide 20: Records and reports on the management of radioactive waste
Further…
f) the classification according to the classification scheme defined for operational purposes;
g) any chemical, or other pathogenic risk associated with the waste and the concentration of hazardous materials;
h) any requirement for special handling due to the risk of criticality, the need for heat extraction or a significantly high dose rate.

## Slide 21: Records and reports on the management of radioactive waste
Required records:
a) radioactive waste generated (date of generation, characteristics of the waste, etc.);
b) stored radioactive waste (including identification, origin, location, physical and chemical and radiological characteristics);
c) materials that have been discharged into the environment (including release data: responsible, etc.);
d) spent or disused radioactive sources returned to the supplier / provider;
e) radioactive waste and disused sources transferred to a waste management facility or to another user;
f) non-conformities and the actions taken in this regard.

## Slide 22: Records and reports on the management of radioactive waste
Example of waste inventory

## Slide 23: Records and reports on the management of radioactive waste
Transfer:
When radioactive waste is transferred to a management facility, the records related to it must be made available to the operator responsible for the next step in the management and there must be a transfer of responsibility document.