## Slide 1: Case studies for Modules 7 and 8
F. Adorján
HAEA (retired)
ferencadorjan@gmail.com

## Slide 2: Elements of the case study
Three tasks are elaborated, they can be applied together or independently, depending on the available time.
Benefits of PSA and DSA, mutual supporting options.
Build a simplified event tree for a selected IE for a notional PWR. Consider some of the necessary fault trees and the required data.
Build up an IRIDM framework for a nuclear safety regulatory body. What elements should be included? How could it be integrated into the Management System of the RB?
Notes: The necessary timeframes for the 3 tasks are different.
The shortest is Task 1. The estimated timeframe is 25 minutes (15 minutes for elaboration and 10 minutes for presentation) + 5 minutes introduction.
For Task 2 the estimated elaboration time is 1 hour, the time for discussion is 10 minutes/group and introduction requires about 10 minutes.
For Task 3 the estimated elaboration time is 0,5 hour, the time for discussion is 5 minutes/group and introduction requires about 10 minutes.
It is estimated that two of three tasks could be covered within the assigned 90 minutes timeframe. It is proposed to take task 2 and 3.

## Slide 3: Method
The participants receive a short introduction of the topic and the task.
The participants elaborate the task in small groups consisting of 3-5 people.
The groups present their results, each presentation is discussed by the other participants and by the lecturer in plenary.

## Slide 4: Introductory remarks for Task 1
The benefits of DSA and PSA were listed and discussed on the presentation. At least 3-3 of them should be listed by the participants.
Concerning the mutual support between DSA and PSA only a limited information was given. Please, try to find such options. The target is to name at least 2-2 such supporting option.
The groups of the participants get 10 minutes to elaborate their solutions. Then in an additional 15 minutes the propositions of each group are to be discussed in plenary.
Notes: The timeframe allocated for the discussion may depend on the number of groups.

## Slide 5: Introductory remarks for Task 2
Consider the following system functions in analysis:
  Scram system
  Startup pumps (one or both pumps available, automatic or manual startup)
  Emergency feed water system (one of two systems available, automatic or manual startup)
End state
OK
OK
CD
ATWS
One startup feed water pump (out of two) is available
A
Scram
S
Loss of feed water
LOFW
One emergency feed water pump (out of two) is available
No.
B
1
2
3
4

## Slide 6: Introductory remarks for Task 2 – Simplifications
Heat is removed either by the condenser or by atmospheric dump valves or main steam safety valves; or by the emergency core cooling system. But for simplicity of the example the corresponding system functions and the possible malfunctions are ignored in the event tree and in the following discussion.
Also: the ATWS (anticipated transient without scram) is a complicated case, it is not to be elaborated here.

## Slide 7: Introductory remarks for Task 2 – Expectations
The groups should elaborate by using natural language the conditions how the initiating event may occur, how was it possible to estimate the probability of the event on the basis of the reliability of the related main components.
Also, by natural language, elaborate the fault trees corresponding to the 3 branching points of the event tree and try to explain how the branching ratios could be evaluated by using the estimated reliability information. Some human actions may also be considered.
Notes: It is also an option, that the presenter explains the first branch, for example as follows:
the scram logic is a highly reliable logic, i.e. about once in 1000 demand may fail. If it fails, still the operator may be fast enough to press the “Big Red Button” in due time, making a manual scram and avoiding any further complication. According to the HRA analysis, the operator fails to act correctly once in every 60 cases. Thus the ATWS branch has a probability of 1/1000 times 1/60 (since the failure of the scram logic and the failure of the operator are independent events), i.e. the probability of the ATWS branch is 1/60000 and the probability of the success branch is 1-1/60000. Note that the actual fault tree may be more complicated.

## Slide 8: Introductory remarks for Task 2 - timing
The groups of the participants get 45 minutes to elaborate their solutions. Then in an additional 20 minutes the solutions of each group are to be discussed in plenary.

## Slide 9: Introductory remarks for Task 3
The details of IRIDM, as we have discussed are directly applicable of the operating organization. However, the IRIDM philosophy and practice can also be applied for regulatory activities. Note, however, that some elements should be skipped in that case. Could there be some additional elements?
The task is to establish the IRIDM process for the regulatory body. Think about the elements, the weighting, the process. Depict the proposed scheme.
Notes: Hints: the economic considerations shouldn’t be included for the RB, but the focusing of regulatory oversight could be included.

## Slide 10: Introductory remarks for Task 3 - timing
The groups of the participants get 30 minutes to elaborate their solutions. Then in an additional 15 minutes the propositions of each group are to be discussed in plenary.

## Slide 11
Thank you!
Notes: Thank you!