## Slide 1: Operational Safety including Operational Feedback
Moazzam Shahzad
Pakistan Nuclear Regulatory Authority (PNRA)
moazzam.shahzad@pnra.org

## Slide 2: Lerning objectives
Understand different requirements which need to be satisfied in order to ensure nuclear power plant operational safety
Recognize the general requirements for the operating organization
State importance of nuclear power commissioning and decommissioning
Importance of Operating Experience Feedback and its utilization

## Slide 3: Contents
IAEA general operational safety requirements
general requirements for the operating organization
purpose of the operational experience feedback
purpose of the emergency preparedness program for NPP
quality assurance program in the nuclear power plant
Identify the training and qualification program of personnel in the nuclear power plant
purpose of the commissioning program in the NPP
Define important programs for safe plant operation.

## Slide 4: Contents
List general requirements for maintenance, testing, surveillance and inspection in the nuclear power plant
Define the term ˝Plant modification˝
Explain the radiation protection and radioactive waste management in the nuclear power plant
Define the purpose of the control of records and reports
Define the purpose of the periodic safety review in the nuclear power plant
State importance of nuclear power plant operation for decommissioning

## Slide 5: Introduction
The responsibility for safety rest with the operating organization
To ensure nuclear safety, safe operation of nuclear power plants is of utmost importance.
Operational safety is a multidisciplinary subject and covers a wide range of topics.
IAEA has published a set of Safety Standards and other technical documents to cover the operational safety and operational experience feedback.
Notes: (Fourth bullet) It is a revision of the Safety Standards Series No. NS-R-2. This standard is also basis for the textbook.
(Fifth bullet) The objective of this textbook is to gather and in one place briefly summarized the various documents which are under the auspices of the IAEA and they deal with operational safety and operational experience feedback.

## Slide 6: Introduction
Most operational safety requirements are derived from the fundamental safety objective of protecting people and the environment, and the related fundamental safety principles (IAEA SF-1):
  Responsibility for safety;
  Role of Government;
  Leadership and management for safety;
  Optimization of protection;
  Limitation of risks to individuals;
  Protection of present and future generations;
  Prevention of accidents;
  Emergency preparedness and response
Notes: Safety objective
The fundamental safety objective is to protect people and the environment from harmful effects of ionizing radiation.
Responsibility for safety
The prime responsibility for safety must rest with the person or organization responsible for facilities and activities that give rise to radiation risks.
  Role of Government
  An effective legal and governmental framework for safety, including an independent regulatory body, must be established and sustained.
Leadership and management for safety
Effective leadership and management for safety must be established and sustained in organizations concerned with, and facilities and activities that give rise to, radiation risks.
Optimization of protection
Protection must be optimized to provide the highest level of safety that can reasonably be achieved.
Limitation of risks to individuals
Measures for controlling radiation risks must ensure that no individual bears an unacceptable risk of harm.
Protection of present and future generations
People and the environment, present and future, must be protected against radiation risks.
  Prevention of accidents
All practical efforts must be made to prevent and mitigate nuclear or radiation accidents.
Emergency preparedness and response
Arrangements must be made for emergency preparedness and response for nuclear or radiation incidents.

## Slide 7: Introduction
The Publication which states the requirements for operational safety is IAEA Specific Safety Requirements No. SSR-2/2.
Objective of this presentation is to briefly summarize the IAEA requirements for operational safety, provide some practical examples on the way they are applied and make reference to additional publications, as appropriate.
Notes: (Fourth bullet) It is a revision of the Safety Standards Series No. NS-R-2. This standard is also basis for the textbook.
(Fifth bullet) The objective of this textbook is to gather and in one place briefly summarized the various documents which are under the auspices of the IAEA and they deal with operational safety and operational experience feedback.

## Slide 8: Introduction
IAEA Operational Safety Requirements (SSR-2/2, Rev.1)
The management and organizational structure of the operating organization
  Primarily responsible for operational safety or nuclear safety, appropriate management system, staffing, structure and functions of the operating organization.
Management of operational safety
Notes: This slides describe the main contents of the IAEA Operational Safety Requirements (SSR-2/2, Rev.1) covered under the heading of the management and organizational structure of the operating organization and Management of operational safety. The further details of these contents will be discussed in next slides.
The management and organizational structure of the operating organization
Primarily responsible for operational safety or nuclear safety, appropriate management system, staffing, structure and functions of the operating organization.
Management of operational safety
Safety polices, Operational Limit and Conditions, training and qualification, performance of safety related activities, monitoring and review of plant performance, control of plant configuration, management of modification, periodic safety reviews, equipment qualification, aging management, records and reports, LTO.

## Slide 9: Introduction
  Operational Safety Programmes
  Considerations of security in plant operation
  Emergency preparedness
  Accident Management Programmes
  Radiation protection and radioactive waste management
  Fire Safety
  Non-radiation-related safety
  Feedback of Operating Experience
Notes:   This slides describe the main contents of the IAEA Operational Safety Requirements (SSR-2/2, Rev.1) covered under the heading of operational safety progemmes. The further details of these contents will be dicsused in next slides.
Considerations of security in plant operation
  → Synergy between safety and security is sought;
Emergency preparedness
  → The plant has to be prepared to respond adequately to nuclear or radiological emergency;
Accident Management Programmes
  → For management of accidents more severe than the design basis accidents;
Radiation protection and radioactive waste management
  → All work must be properly planned and implemented;
Fire Safety
  → Programmes and procedures have to be in place to ensure fire safety;
Non-radiation-related safety
  → Industrial safety;
Feedback of Operating Experience
  → The operating organization establishes an operating experience programme to learn from events at the plant and events in the nuclear industry and other industries worldwide.

## Slide 10: Introduction
  Plant Commissioning
  Commissioning programme, tests, amendments to plant design documentation;
  Plant operations
  Operating instructions and procedures;
  Operation Control rooms and control equipment;
  Material conditions and housekeeping;
  Chemistry programme;
  Core management and fuel handling;
Notes: (Second sub-bullet) Feedback of Operating Experience
The operating organization establishes an operating experience programme to learn from events at the plant and events in the nuclear industry and other industries worldwide.

## Slide 11: Introduction
  Maintenance, testing, surveillance and inspections
  Only well maintained equipment, can carry out the required functions;
  Maintenance, testing, surveillance and inspections programmes, procedures, practices and outage programmes;
  Decommissioning
  Preparation for decommissioning, including for radiation protection and radioactive waste management.

## Slide 12
Safety of Nuclear Power Plant Operation

## Slide 13: The management and organizational structure of the operating organization
Responsibilities of the operating organization
prime responsibility for nuclear safety,
may delegate authority,
policy on nuclear safety,
documented organizational structure,
regular reviews of the operation;
Management system
Quality assurance programme → all activities;
Quality assurance → used systematically;
Notes: (First title) Responsibilities of the operating organization:
The operating organisation has prime responsibility for nuclear safety.
May delegate authority to the plant management for the safe operation of the plant.
A policy on nuclear safety is developed by the operating organization and implemented by all site personnel.
A documented organizational structure must be established by the operating organization.
Safety culture is one of the selection criteria when hiring or promoting managers.
Ensures regular reviews of the operation of the nuclear power plant.
(Second title) Management system
A comprehensive quality assurance programme covers all activities which may affect the safe operation.
Quality assurance is used systematically in:
Management processes;
Operational activities;
Assessments of management processes and of the adequacy of operational performance.

## Slide 14: The management and organizational structure of the operating organization
Structure and functions of the operating organization
established and documented
    → roles and responsibilities
Staffing of the operating organization
  competent managers,
  sufficient qualified personnel,
  responsibility:
    → necessary knowledge,
    → skills,
    → attitudes, and
    → safety expertise;
Notes:   (First title) The structure of the operating organization and the functions, roles and responsibilities of its personnel shall be established and documented.
  (Second title) The operating organization is staffed with competent managers and sufficient qualified personnel for the safe operation of the plant.
  (Second title/Third sub-bullet) The operating organization is responsible for ensuring that the necessary knowledge, skills, attitudes and safety expertise are sustained at the plant, and that long term objectives for human resources policy are developed and are met.

## Slide 15: The management and organizational structure of the operating organization
Interface with the Regulatory Body
Important for safe operation of nuclear power plant;
Essential to the achievement of common objective;
Assistance and access to the plant and documentation;
Physical Protection
prevent persons from deliberately carrying out unauthorized actions;
plans and procedures for physical protection of the site;
Notes: (First title) Interface with the Regulatory Body
Independent regulatory body is important for safe operation of nuclear power plant.
It is essential to the achievement of common objective, i.e. safe operation.
The operating organization gives it all necessary assistance and access to the plant and documentation.
(Second bullet) Physical Protection
Precautions must be taken to prevent persons from deliberately carrying out unauthorized actions that could jeopardize safety.
The operating organization has plans and procedures for physical protection of the site.

## Slide 16: Management of operational safety
Safety policy
Give safety the highest priority;
Policy gives safety the utmost priority;
Key aspects of the safety policy;
Operational limits and conditions (OLCs)
Developed → plant operates in accordance with design assumptions and intent;
OLCs → important part of the basis;
All deviations → documented and reported, actions are taken;
Notes:   (First title) Safety policy
    The operating organization establishes and implements operational policies that give safety the highest priority.
    The operational policy established and implemented by the operating organization gives safety the utmost priority, overriding the demands of production and project schedules. The safety policy promotes a strong safety culture, including a questioning attitude and a commitment to excellent performance in all activities important to safety. Managers promote an attitude of safety consciousness among plant staff.
    Key aspects of the safety policy are communicated to external support organizations, including contractors, so that the operating organization’s requirements and expectations for the safety related activities of external support organizations, including contractors, will be understood and met.
    The safety policy of the operating organization includes a commitment to achieving enhancements in operational safety. The strategy of the operating organization for enhancing safety and for finding more effective ways of applying and, where feasible, improving existing standards is continuously monitored and supported by means of a clearly specified programme with clear objectives and targets.
(Second title) Operational limits and conditions (OLCs)
Are developed to ensure that the plant operates in accordance with design assumptions and intent.
OLCs can be classified as:
Safety limits;
Limits on safety system settings;
Limits and conditions for normal operation and for safe transient operational states;
Surveillance and testing requirements;
Action statements for deviations from normal operation.
OLCs are important part of the basis on which the operating organization is authorized to operate the plant.
All deviations from OLCs are documented and reported, and appropriate actions are taken.

## Slide 17: Management of operational safety
Qualification and Training of personnel
  Qualifications and experience criteria of personnel;
  Suitably qualified personnel;
  Formal authorization → under the jurisdiction of the regulatory body;
Performance of safety related activities
  Safety related activities → adequately analysed and controlled;
Monitoring and review of safety performance
  System for continuous monitoring and periodic review;
Notes: (First title) Qualification and Training of personnel
The operating organization must define the qualifications and experience criteria of personnel.
Suitably qualified personnel must be selected.
Personnel must get necessary training and instruction.
Persons performing functions important to safety are required to hold a formal authorization which is under the jurisdiction of the regulatory body.
Production requirements must not be in conflict with the conduct of the training programme.
For each major group of personnel is developed and implemented programme for initial and continuing training.
(Second title) The operating organization ensures that safety related activities are adequately analysed and controlled to ensure that the risks associated with harmful effects of ionizing radiation are kept as low as reasonably achievable.
  (Third title) The operating organization establishes a system for continuous monitoring and periodic review of the safety of the plant and of the performance of the operating organization.

## Slide 18: Management of operational safety
  Control of plant configuration
Establishing and implementing → system for plant configuration management;
Plant modifications
Modifications → categorized and approved;
Temporary modifications → identified;
Modifications relevant to safe operation → submitted to the regulatory body;
Notes: (First title) The operating organization shall establish and implement a system for plant configuration management to ensure consistency between design requirements, physical configuration and plant documentation.
(Second title) Plant modifications
All modifications must be categorized according to their safety significance and approved.
Temporary modifications must be clearly identified at the point of application.
Modifications which are relevant to safe operation are submitted to the regulatory body.
Modifications must be installed and tested in accordance with the work control system and testing procedures.
Information about plant modifications must be given to the operating personnel.

## Slide 19: Management of operational safety
Periodic safety review (PSR)
A systematic safety reassessment of the plant → performed
Validation of existing safety report;
PSR takes into account:
  actual status of the plant, operating experience, predicted end‑of‑life state, current analytical methods, current safety standards, and current knowledge;
Base for implementation of any necessary corrective actions and modifications;
Notes: (First bullet) A systematic safety reassessment, which may be fulfilled by a periodic safety review (PSR), of the plant must be performed by the operating organization throughout its operational lifetime, with account taken of operating experience and significant new safety information from all relevant sources.
(Second bullet) The PSR determines to what extent the existing safety report remains valid.
(Third bullet) It takes into account the actual status of the plant, operating experience, predicted end‑of‑life state, current analytical methods, current safety standards and current knowledge.
(Fourth bullet) Based on the results of the systematic safety reassessment the operating organization implements any necessary corrective actions and any reasonably practical modifications to move towards current standards.

## Slide 20: Management of operational safety
  Equipment qualification
Systematic assessment;
  Ageing management
An effective ageing management programme;
Control of records and reports
Arrangements for control of records and reports;
Latest version → used by personnel;
Off‑site storage of essential documents;
  Programme for long term operation
Programme for ensuring the long term safe operation;
Notes: (First bullet) The operating organization ensures that a systematic assessment is carried out to provide reliable confirmation that safety related items are capable of the required performance for all operational states and for accident conditions.
(Second bullet) The operating organization ensures that an effective ageing management programme is implemented to ensure that required safety functions of systems, structures and components are fulfilled over the entire operating lifetime of the plant.
(Third bullet) The operating organization makes arrangements for control of records and reports important to safety in accordance with the established quality assurance system.
(Fourth bullet) The document management system ensures that only the latest version of each document is used by personnel.
(Fifth bullet) Off‑site storage of essential documents, such as the emergency plan, for use in the event of an emergency situation must be considered.
  (Sixth bullet) Where applicable, the operating organization establishes and implements a comprehensive programme for ensuring the long term safe operation of the plant beyond a time-frame established in the licence conditions, design limits, safety standards and/or regulations.

## Slide 21: Operational safety programmes
Consideration of objectives of nuclear security in safety programmes
implementation of safety and security requirements;
Emergency preparedness
Prepares/establishes → emergency plan;
Plan covers all activities within its responsibilities → in the event of an emergency;
Scheduled exercises of the emergency plans;
Equipment, documentation and communication → available and well-maintained.
Notes: (First bullet) The operating organization ensures that the implementation of safety requirements and security requirements satisfies both safety objectives and security objectives. The operating organization is responsible for managing the implementation of safety requirements and security requirements by ensuring close cooperation between safety managers and security managers, with the objective of minimizing risks.
(Second title) Emergency preparedness
The operating organization prepares/establishes an emergency plan.
Plan covers all activities within its responsibilities, to be carried out in the event of an emergency.
Plan also includes arrangements for emergency situations involving a combination of non‑nuclear and nuclear hazards.
Personnel must be trained in the performance of their duties in an emergency.
Scheduled exercises of the emergency plans.
All equipment, documentation and communication systems that are used in emergency situations must be available and well-maintained.

## Slide 22: Operational safety programmes
    Accident management programme
For the management of beyond design basis accidents;
    Radiation protection and management of radioactive waste
programme accordance with ALARA;
Enough independence and resources;
Exposure measured, assessed and recorded;
Generation of radioactive waste → minimum;
Procedures for monitoring and controlling
Notes:   (First bullet) The operating organization establishes an accident management programme for the management of beyond design basis accidents.
(Second bullet) Nuclear power plant must have a programme which is in accordance with ALARA principle.
(Third bullet) The radiation protection function must have enough independence and resources.
  (Fourth bullet).Personnel who may be occupationally exposed to radiation must have their exposure measured, assessed and recorded. Dose records are kept as required and made available to the regulatory body.
(Fifth bullet) The generation of radioactive waste, in terms of both activity and volume, must be kept to the minimum practicable by appropriate operating practices.
(Sixth bullet) The operating organization must establish and implement procedures for monitoring and controlling discharges of radioactive effluents and perform a safety analysis for radioactive discharges which demonstrates that the assessed radiological impact and the exposure to the general public are kept as low as reasonably achievable.

## Slide 23: Operational safety programmes
Fire safety
Fire safety arrangements → based on a periodically updated fire safety analysis;
    Non-radiation-related safety
A programme established and implemented;
    Operational experience feedback
To learn from events;
Helps to maintain nuclear safety;
Provides lessons for the operation;
Data → collected and retained;
Notes: (First bullet) The operating organization must have fire safety arrangements, based on a periodically updated fire safety analysis. Fire arrangement in generally includes:
the application of the principle of defence in depth,
the impact of plant modifications on fire-fighting,
the control of combustibles and ignition sources,
the inspection, maintenance and testing of fire protection measures,
the establishment of manual fire-fighting capability, and
the training of plant personnel.
(Second bullet) The operating organization establishes and implements a programme to ensure that safety related risks associated with non-radiation-related hazards to personnel involved in activities at the plant are kept as low as reasonably achievable.
Non-radiation-related safety concerns hazards other than radiation related hazards; this is sometimes referred to as industrial safety or conventional safety.
(Third bullet) The operating organization establishes an operating experience programme to learn from events at the plant and events in the nuclear industry and other industries worldwide.
(Fourth bullet) Operational experience feedback helps to maintain nuclear safety.
(Fifth bullet) The operating organization obtains and evaluates information from operational experience at other plants which provides lessons for the operation of their own plant.
(Sixth bullet) Data from operating experience are collected and retained for use as input to plant ageing management, residual life evaluation, probabilistic safety assessment and periodic safety review.

## Slide 24: Plant commissioning
Commissioning programme provides
  evidence → NPP as constructed meets the design intent;
  complies → safety requirements;
The interfaces between groups → defined and controlled;
Operating procedures → verified
  prior to loading fuel;
Prior to the initial core loading is necessary to confirm all prerequisites.
Notes: (First bullet) Commissioning programme provides an evidence that the NPP as constructed meets the design intent and complies with the safety requirements.
(Second bullet) The interfaces between groups involved in commissioning is clearly defined and properly controlled.
(Third bullet) Operating procedures must be verified prior to loading fuel into the core.

## Slide 25: Plant operations
Operating procedures
All activities → in accordance with procedures;
Operating procedures cover
  normal, abnormal and emergency operating conditions;
Operation control rooms and control equipment
Operation control rooms and control equipment
  maintained → suitable condition;
Habitability and good condition;
  Material conditions and housekeeping
maintain → high standard of material conditions,…
Notes: (First bullet) All activities are conducted in accordance with established procedures.
(Additional text to first bullet) A comprehensive administrative procedure must be established, which contains the rules of development, elaboration, validation, acceptance, modification and withdrawal of operating instructions and procedures.
(Second bullet) Operating procedures are developed which provide comprehensive coverage of normal, abnormal and emergency conditions, in accordance with the policy of the operating organization and the requirements of the regulatory body.
  (Third bullet) The operating organization ensures that the operation control rooms and control equipment are maintained in a suitable condition.
  (Fourth bullet) The habitability and good condition of control rooms is maintained. Where the design of the plant foresees additional or local control rooms that are dedicated to the control of processes that could affect plant conditions, clear communication lines are developed for ensuring an adequate transfer of information to the operators in the main control room.
(Fifth bullet) The operating organization develops and implements programmes to maintain a high standard of material conditions, housekeeping and cleanliness in all working areas.
(Additional text to fifth bullet) Administrative controls shall be established to ensure that operational premises and equipment are maintained, well lit and accessible, and that temporary storage is controlled and limited. Equipment that is degraded is:
identified,
reported,
and corrected in a timely manner.

## Slide 26: Plant operations
  Chemistry programme
Necessary support for chemistry and radiochemistry;
Developed prior to normal operation and is in place during the commissioning programme
  Core management and fuel handling
Arrangements for activities → core management and on‑site fuel handling;
Established → design intent and assumptions;
Criteria and procedures → dealing with fuel and control rod failures;
Notes: (First bullet) The operating organization establishes and implements a chemistry programme to provide the necessary support for chemistry and radiochemistry.
(Second bullet) The chemistry programme is developed prior to normal operation and is in place during the commissioning programme. The chemistry programme provides the necessary information and assistance for chemistry and radiochemistry for ensuring:
safe operation,
long term integrity of structures, systems and components,
and minimization of radiation levels.
(Third bullet) The operating organization is responsible and make arrangements for all the activities associated with core management and on‑site fuel handling.
(Fourth bullet) A fuelling programme is established in accordance with the design intent and assumptions.
(Fifth bullet) Criteria must be established and procedures written for dealing with fuel and control rod failures to minimize fission and activation products in the primary coolant or in gaseous effluent.

## Slide 27: Maintenance, testing, surveillance and inspection
Programme for structures, systems and components → important to safety;
Procedures → in accordance with administrative procedures.
Work planning and control system is implemented
Abnormal event → revalidation
Data → recorded, stored and analysed;
Outage management
Effective performance, planning and control of work activities;
Notes: (First bullet) A programme of maintenance, testing, surveillance and inspection of those structures, systems and components which are important to safety, is needed.
(Second bullet) Procedures for all maintenance, testing, surveillance and inspection tasks are in accordance with established administrative procedures.
(Third bullet) A comprehensive work planning and control system is implemented to ensure that work is properly authorized, and carried out in accordance with procedures.
(Fourth bullet) Following any abnormal event an revalidation of the safety functions and functional integrity of any component or system which may have been challenged by the event must be done.
(Fifth bullet) Maintenance, testing, surveillance and inspection data must be recorded, stored and analysed.
(Sixth bullet) The operating organization establishes and implements arrangements to ensure the effective performance, planning and control of work activities during outages.
(Additional text to sixth bullet) Outage planning is a continuing, improving process involving past, present, next scheduled and future outages. The tasks, authorities and responsibilities of the groups and persons involved in preparing, conducting or assessing outage schedules and activities are set out in writing and are followed by all the plant staff and contractor staff who are involved. The interfaces between the group responsible for outages and other groups, including groups on the site and off the site, shall be clearly defined. Operating personnel shall be kept informed of current activities for maintenance, modification and testing.

## Slide 28: Preparation for decommissioning
Arrangements → well in advance of the final shut-down;
Experiences → essential in order to facilitate the planning of decommissioning;
Safety analysis report → revised
  safety justification during decommissioning;
Safety analysis report → scrutinized;
OLCs requirements → implemented
  given decommissioning stage;
Notes: (First bullet) The operating organization must have in place arrangements for decommissioning the plant well in advance of the final shut-down.
(Second bullet) Experience from handling contaminated or irradiated structures, systems and components during maintenance or modification of the plant must be recorded in order to facilitate the planning of decommissioning.
(Third bullet) The safety analysis report must be revised, or an equivalent report is prepared, to provide the safety justification during the various stages of decommissioning.
(Fourth bullet) The safety analysis report must be scrutinized to derive Operational limits and Conditions (OLC), surveillance and inspections during decommissioning.
(Fifth bullet) As a given decommissioning stage is entered, the relevant OLC requirements must be implemented.

## Slide 29: Discussion Questions
  Who has prime responsibility for operational safety?
  Who is responsible for independent supervision of the nuclear power plant?
  To whom the operating organization reports abnormal events?
  What is an important reason for collecting data from operational experiences?
  What is role of the operating organization during the commissioning?
Notes: Answer 1:
The operating organisation has prime responsibility for nuclear safety. The operating organization may delegate authority to the plant management for the safe operation of the plant, but it retains prime responsibility for nuclear safety. In such cases the operating organization must provide the necessary resources and support
Answer 2:
The independent regulatory body is important for safe operation of nuclear power plants, because of its supervisory role. It is essential to the achievement of their common objective, i.e. safe operation of nuclear power plants, that there is mutual understanding and respect between the regulatory body and the operating organization in order to support a frank and open but formal relationship.
Answer 3:
The operating organization must develop and implement a procedure for reporting abnormal events to the regulatory body in accordance with established criteria. If the request of the regulatory authority could have an adverse effect on safety, then, in view of the prime responsibility for safety, this opinion of the operating organization must be presented to the regulatory body as a basis for further discussions.
Answer 4:
Operational experience at the plant is assessed in a systematic way. Similarly, the operating organization obtains and evaluates information from operational experience at other plants which provides lessons for the operation of their own plant. Exchange of experience and contribution to national and international organizations is very important. Operational experience feedback helps to maintain nuclear safety.
Answer 5:
The comprehensive commissioning programme is established to provide evidence that the nuclear power plant as constructed meets the design intent and complies with the safety requirements. The operating organization must ensure that the commissioning programme includes all the tests necessary to demonstrate that the plant as installed meets the requirements of the safety analysis report, and satisfies the design intent and consequently can be operated in accordance with the Operating Limits and Conditions (OLCs).

## Slide 30
Expectations for Operational Safety

## Slide 31: Management, organization and administration
Organizational structure → support safe, reliable and effective performance and control;
Responsibilities and authorities for accomplishing assigned tasks
  clearly defined and communicated;
Management monitoring and assessment → integral parts of the administrative system;
Safety management → needed to promote
  strong safety culture;
  achieve and maintain good safety performance;
Notes: (First bullet) The organizational structure must support safe, reliable and effective performance and control of all nuclear power plant (NPP) activities.
(Second bullet) Responsibilities and authorities for accomplishing assigned tasks must be clearly defined and communicated within the established organizational structure.
(Third bullet) Management monitoring and assessment activities are integral parts of the administrative system.
(Fourth bullet) At the power plant it must be established a sound safety management system, as an integral part of the overall management system. That safety management is needed to promote a strong safety culture and achieve and maintain good safety performance.

## Slide 32: Management, organization and administration
Organization and administration
Organizational plan → indicates the general policies, lines of responsibility and authority, etc.
Functional responsibilities, levels of delegated authority and lines of internal and external communication → defined in writing;
Adequate financial and manpower resources and facilities;
Qualified spares, materials and equipment;
Individuals → physically and mentally fit;
Notes: (First bullet) The operating organization must establish an organizational plan that indicates the general policies, lines of responsibility and authority, etc., needed to run the nuclear power plant. When some critical plant personnel may leave the workforce, management must have plans for filling the openings with competent people.
(Second bullet) Functional responsibilities, levels of delegated authority and lines of internal and external communication must be clearly defined in writing.
(Third bullet) For safe and efficient operation of the plant managers must have an adequate financial and manpower resources and facilities.
(Fourth bullet) Qualified spares, materials and equipment must be on the stockpile needed for timely execution of safety-related activities.
(Fifth bullet) The management system is supported by a well-established human resources management programme, a well-established performance appraisal system, and a promotion and succession-planning system that takes into account safety culture. Individuals must be physically and mentally fit to perform their job in a safe manner.

## Slide 33: Management, organization and administration
Contractors → same standards of quality and safety policy;
The regulatory body for its work needs access to the plant and documents.
Management activities
Establish and communicate → high standards of performance;
Promote and reinforce → policies, safety goals and objectives;
Plant staff → mechanism to report safety concerns;
Managers → routinely in the field;
Notes: (First bullet) Support activities carried out by contractors must be in accordance with the applicable standards of quality and safety policy. Requirements relating to quality and competency of the contractor staff and work product must be at the same standard as the activities carried out by the plant staff.
(Second bullet) The operating organization must allow access to the plant and documents, that the regulatory body may perform its work.
(Third bullet) Management must establish and clearly communicate high standards of performance.
(Fourth bullet) They must actively promote and frequently reinforce corporate policies, safety goals and objectives.
(Fifth bullet) Plant staff must have a mechanism to report safety concerns to management. Staff must have a similar mechanism with which can report safety concerns to an independent body (e.g. regulator).
(Sixth bullet) Managers are routinely in the field that could assess and discuss the conduct of work and compliance with management objectives.

## Slide 34: Management, organization and administration
Management of safety
Integral part → overall management system;
Safety policy demonstrates → commitment to high safety performance;
Plant operation is monitored
  license accountability,
  evaluation of goals and objectives;
Quality assurance programme
Tool for the management → verify or confirm requirements;
Independent assessments → on behalf of management;
Notes: (First bullet) The organization's safety management system is generally considered to be an integral part of its overall management system.
(Additional text to first bullet) A safety management system is applied in a coherent manner, with integrating management of safety, health, environmental quality and economic matters.
(Second bullet) A policy on safety is developed by the operating organization and applied by all site personnel. The safety policy demonstrates the organization's commitment to high safety performance.
(Third bullet) Plant operation must be comprehensively monitored to ensure license accountability and to evaluate the goals and objectives established for safe operation of the plant.
(Fourth bullet) The QA programme is a tool for the management that can verify or confirm the requirements.
(Additional text to fourth bullet) Programme includes details of how work is to be managed, performed and assessed. Quality assurance requirements apply to activities such as:
operations,
maintenance and procurement of replacement items, etc.
(Fifth bullet) Independent assessments must be conducted on behalf of management to measure the effectiveness of management processes and the adequacy of work performance, to monitor item and service quality and to promote improvement.

## Slide 35: Management, organization and administration
Industrial safety programme
General policy → ensure the industrial health and safety;
  Elements → documented;
Senior management → committed;
  Authority and responsibility → industrial safety performance;
Document and records management
Ensure appropriate keeping of all relevant documents;
Records → specified, prepared, authenticated and maintained;
Records storage system → established;
Notes: (First bullet) The operating organization must have a general policy to ensure the industrial health and safety of personnel on site is satisfactory. All elements of this policy are documented in a plant safety manual, while details are included in implementing procedures.
(Second bullet) Senior management is committed to industrial safety and the line supervisors must have the authority and responsibility to ensure good industrial safety performance. A risk analysis must be performed prior to any activity.
(Third bullet) A document and records management system must be established to ensure the appropriate keeping of all documents relevant to the safe and reliable operation of the plant, including design documents, commissioning documents, documents related to the operational history of the plant, as well as general and specific procedures.
(Fourth bullet) The records system ensure that records are specified, prepared, authenticated and maintained, as required by applicable administrative procedures in accordance with the QA requirements. Information sources are integrated, when appropriate, to improve the accuracy, timeliness and availability of the information.
(Fifth bullet) A suitable records storage system must be in place to ensure safe conservation and easy accessibility of all documents and records necessary to operate the plant.

## Slide 36: Training and qualification
Adequate number of highly qualified and experienced personnel;
  Training and qualification → under constant review;
  Responsibility → appropriate training;
  Continuing training;
Training policy and organization
Overall training policy;
  Known, understood and supported;
  Training plan → long term needs and goals;
Qualifications and training of external personnel;
Notes: (First bullet) NPPs are required to be staffed by an adequate number of highly qualified and experienced personnel.
Training and qualification programmes must be established and kept under constant review.
The operating organization has the responsibility to ensure that all plant personnel must receive appropriate training.
Qualifications are maintained by participation in continuing training programmes.
(Second bullet) The operating organization formulates an overall training policy. The training policy must be known, understood and supported by all persons concerned. A training plan is prepared on the basis of the long term needs and goals of the plant.
(Additional text to second bullet) A system to identify the training needs of all staff must be in place. Training needs must be reviewed and revised to take account of organizational changes and changes in plant and processes.
(Third bullet) The operating organization must ensure that the qualifications and training of external personnel performing safety related duties are adequate for the functions to be performed.

## Slide 37: Training and qualification
Quality of the training programmes
Performance based programmes for initial and continuing training;
  Content → based on a systematic approach;
  Periods of formal training in the classroom, intervals of simulator, or laboratory, or workshop and practical training in the plant;
  Design of the programme → updating;
Training programmes for control room operators (CROs) and shift supervisors (SSs)
Develop and improve the competence to operate the controls;
  Broad knowledge of the fundamentals;
Notes: (First bullet) Performance based programmes for initial and continuing training must be developed and put in place for each major group of personnel.
The content of each programme is based on a systematic approach, such as job and task analysis, ensuring the necessary knowledge and skills are incorporated.
Training programmes for most NPP positions include periods of formal training in the classroom intermixed with intervals of simulator, or laboratory, or workshop, training and should include practical training in the plant.
Training is to be conducted and evaluated in the work environment by qualified, designated individuals.
(Second bullet) Design of the programme must allow updating when changes in the tasks, plant systems or procedures are made.
(Additional text to second bullet) The adequacy of all training programmes must be periodically reviewed and assessed by both plant management and the training staff. This includes evaluation of training graduate competence in the workplace and adjustment of training programmes as necessary.
(Third bullet) The training and qualification programme for control room operator (CRO) and shift supervisor (SS) must develop and improve the competence to operate the controls of a nuclear power plant.
(Additional text to third bullet) Programme ensures that they are able to:
  monitor and control the plant systems status (in accordance with technical specifications, etc.),
  conduct all operations in a safe and reliable manner (without causing excessive thermal or mechanical load), and
  take correct actions (in case of various abnormal and emergency conditions).
(Fourth bullet) The training programmes also include broad knowledge of the fundamentals to provide basis for understanding the operation of systems and integrated plant operations and to diagnose system/component problem.

## Slide 38: Training and qualification
Training programmes for field operators
Develop, maintain and improve the knowledge and skills → outside the control room;
  Programme → similar as the programme for control room
  → monitor performance and status,
Training programmes for maintenance personnel
Develop and maintain or improve the knowledge and skills → for carrying out preventive and predictive maintenance;
Experience of faults and hazards → reviewed and incorporated into training programmes;
Notes: (First bullet) The field operator training and qualification programme must develop, maintain and improve the knowledge and skills necessary to operate equipment outside the control room, as directed by the control room staff.
Programme must be similar as the programme for control room operators. Programme ensures that they are able to:
  monitor the equipment performance and status,
  conduct all field operations in a safe and reliable manner, and
  detect and properly respond to plant conditions;
(Second bullet) Programme must develop and maintain or improve the knowledge and skills necessary for carrying out preventive and predictive maintenance. Programmes include:
plant layout and the general features and purposes of plant systems,
quality assurance and quality control,
maintenance procedures and practices, including surveillance and inspections, and
special maintenance skills.
(Third bullet) Experience of faults and hazards caused by errors in maintenance procedures must be reviewed and incorporated into training programmes.

## Slide 39: Training and qualification
Training programmes for technical plant support personnel
Knowledge and skills to support safe and reliable plant operation
  plant systems and operational methods;
  operational features
Training programmes for management and supervisory personnel
Adequate number of experienced and qualified staff;
Understanding of relevant standards, rules and regulations
Notes: (First bullet) Programmes must be established to develop and maintain the knowledge and skills to support safe and reliable plant operation.
Personnel acquires knowledge of plant systems and understanding of operational methods and environment.
Personnel should have knowledge of the operational features of the plant.
Programmes cover such subject areas as:
  reactor physics and core management,
  chemistry,
  radiation protection, etc.
(Second bullet) Management development programme must ensure an adequate number of experienced and qualified staff, which can fill any manager or supervisor position.
Programme emphasizes the concept and practices of safety culture.
Programmes also emphasize the special problems of managing an NPP (demand for safety and the familiarity with emergency procedures).
(Third bullet) Programme gives them understanding of relevant standards, rules and regulations.
Special attention is given to gaining from the benefits of operational experience feedback.
The managers and supervisors also attend continuing training in their areas of responsibility.

## Slide 40: Training and qualification
Training programmes for training group personnel
Training commensurate with duties and responsibilities
  training instructors → technically competent and have credibility,
  understand all aspects of the content,
  maintain → technical and instructional competence;
General employee training (GET)
All new employees → introduced into the organization and their work environment;
  Refresher training → periodically;
Notes: (First bullet) All training department staff must be given training commensurate with their duties and responsibilities.
Training instructors are technically competent and have credibility with the trainees and other plant personnel.
They must understand all aspects of the content being taught and the relationship to overall plant operation.
Instructors must be familiar with the basics of adult learning and have adequate instructional and assessment skills.
Instructors must maintain their technical and instructional competence.
(Second bullet) All new employees who starting work must be introduced into the organization and their work environment. GET gives them:
a basic understanding of their responsibilities and safe work practices,
the importance of quality programmes and following procedures, and
the practical abilities to protect themselves.
  (Third bullet) Refresher training on GET topics must be periodically provided.

## Slide 41: Operations
Operations involve activities that supervise the operating group.
  Main function → safe and efficient operation;
  Direct impact on the reactor operation;
  Group → composed of shift crews and supporting staff;
Organization and functions
Safe and conservative operation of the NPP;
Number of operations personnel must be sufficient;
Operations goals and objectives → written and defined;
Plant management → committed to nuclear safety;
Notes: (First bullet) Operations involve activities that supervise the operating group.
Operations main function is to run the plant safely and efficiently.
The operating group has a direct impact on the reactor operation.
The group is normally composed of shift crews and supporting staff during office hours.
During off-hours the shift supervisor maintains the authority of the plant manager.
(Second bullet) The organization and functions of the operating group must ensure safe and conservative operation of the NPP under all operational states and accident conditions.
(Third bullet) Number of operations personnel must be sufficient for the safe and reliable operation.
(Fourth bullet) The operations goals and objectives must be written and defined.
(Fifth bullet) Plant management must be clearly committed to nuclear safety.

## Slide 42: Operations
Operations facilities and operator aids
Facilities and equipment → well maintained and adequate;
Operating rules and procedures
Procedures → plant operates within the OLCs
  approved by plant management,
  controlled by established procedures, and
  implemented in a timely manner;
  Multiple unit site → documents and procedures should be located at each unit;
Notes: (First bullet) The facilities and equipment used by the operating staff must be well maintained and adequate. The plant has a programme to control operator aids on the plant. This programme ensures:
reliable communications,
well identified and labelled equipment,
clear of defective or unavailable equipment,
good environmental conditions at the plant,
clear and ever friendly information systems, and
adequate and well maintained supportive equipment.
(Second bullet) Operating personnel must operate the plant safely and reliably while keeping the plant's operation within the OLCs. Procedures are developed for normal operation to ensure that the plant is operated within the OLCs. All procedures must be:
approved by plant management,
controlled by established procedures, and
implemented in a timely manner.
(Third bullet) At a multiple unit site, documents and procedures must be located at each unit.

## Slide 43: Operations
Conduct of operations
Personnel → cognizant of and have control over the plant
  Shift supervisor → informed of all the plant activities;
A policy → gives direction how to use a procedure;
  Procedure users → encouraged to provide feedback;
Control room activities → in a business-like and professional manner;
Effective reviews → after a reactor trip or unplanned shutdown;
Notes: (First bullet) Operations personnel must be cognizant of and have control over the status of plant systems and equipment. The shift supervisor must be informed of all the plant activities and it is similarly for the operators.
(Second bullet) A policy must be in place that gives direction how a procedure must be used. Procedure users must be encouraged to provide feedback to procedure writers.
(Third bullet) Control room activities must be conducted in a business-like and professional manner.
Control room access is limited to persons on official business only.
The shift crews routinely monitor the condition of the plant and make the appropriate records.
The shift turnovers must be carried out in accordance with the formal procedure.
(Fourth bullet) Effective reviews must be conducted after a reactor trip or unplanned shutdown.

## Slide 44: Operations
Work authorizations
Work → planned, analysed and executed
  consistent with the requirements;
Operations group → responsibility to assist maintenance;
Emergent work → through the safety review;
Fire prevention and protection programme
Plant personnel → qualified and trained;
Periodically drills and exercises;
Full consultation and liaison → with any off-site organizations;
Notes: (First bullet) Work conducted at the plant is planned, analysed and executed in a manner that is consistent with the requirements of plant operations. A work control process must be integrated into all work groups.
(Second bullet) The operations group has the responsibility to assist maintenance in the planning and execution of work.
(Third bullet) Emergent work must go through the safety review process.
(Additional text to first title) Planning of work, outages, modifications and tests must be well coordinated.
The results of risk assessment need to be incorporated into the documentation.
(Fourth bullet) Responsibilities of site staff involved in the establishment, implementation and management of the programme, including arrangements for any delegation of responsibilities, must be identified and documented.
Plant personnel must be appropriately qualified and trained.
(Fifth bullet) Periodically, drills and exercises must be conducted.
(Sixth bullet) Full consultation and liaison must be maintained with any off-site organizations.
(Additional text to second title) It is expected that the programme includes at least the following:
Control procedures for combustible materials and ignition sources;
Inspection, maintenance, surveillance and testing of fire protection measures;
Manual firefighting capability;
Emergency plans (including liaison with any off-site organizations);
Integration of plant fire safety arrangements and liaison between parties involved;
Review of plant modifications;
Training;
Impact of plant modifications on fire safety;
Periodic updating of the fire hazard analysis.

## Slide 45: Operations
Management of accident conditions
Arrangements and procedures → actions following accident conditions;
Organization and administration → control of NPP under accident conditions;
  Shift supervisor → prompt support from the technical staff;
Training and drills → using the emergency operating procedures;
  The emergency staff and the supporting groups → trained in performing appropriate, pre-planned actions.
Notes: (First bullet) Arrangements and procedures must be in place which address the actions necessary following accident conditions at a plant.
(Second bullet) The organization and administration of the operating group must ensure that the NPP can be controlled under accident conditions.
The shift supervisor must have prompt support from the technical staff.
Under extreme situations an operator may be required to deviate from OLCs.
(Third bullet) Training and frequent drills using the emergency operating procedures must be carried out.
The emergency staff and the supporting groups must be trained in performing appropriate, pre-planned actions.

## Slide 46: Maintenance
Maintenance → in-service inspection, spare parts, materials and outage management;
Nuclear installations → regularly inspected, tested and maintained;
Organization and functions
Goals, objectives and priorities → consistent with the plant policies and objectives.
Feedback from performance results;
Plant's staff and contractor's;
  Contractor personnel → same criteria;
Notes: (First bullet) Maintenance covers in-service inspection, spare parts, materials and outage management
All nuclear installations must be regularly inspected, tested and maintained in accordance with approved procedures. Maintenance ensures that components, structures and systems continue to be available and to operate as intended, and that they retain their capability to meet the design objectives and the requirements of the safety analysis. The operating organization must prepare and implement a programme of maintenance, testing, surveillance and inspection of those structures, systems and components which are important to safety.
(Second bullet) The nuclear installations must be regularly inspected, tested and maintained.
Maintenance ensures that all components continue to be available and to operate as intended, and that they retain their capability to meet the design objectives and the requirements.
(Third bullet) Goals, objectives and priorities of the maintenance department must be defined to be consistent with the plant policies and objectives.
(Fourth bullet) Feedback from performance results is used in accountability reviews and in establishing goals and objectives for subsequent planning periods.
(Fifth bullet) During the outage, work could be performed by the plant's staff and the supervision of contractor's work.
Contractor personnel must be subject to the same criteria.
(Additional text to fifth bullet) Employment of contractors have financial benefits, but it often comes at the expense of safety. Therefore, emphasis must be placed on the quality and safety of work done by the contractor.

## Slide 47: Maintenance
Maintenance facilities and equipment
Maintenance facilities
  → provide sufficient space and equipment;
  → clean and orderly;
Maintenance programmes
Optimizing safe and reliable performance over the lifetime of the plant;
Preventive maintenance (PM) minimizes the potential for breakdown
Notes: (First bullet) Working facilities must provide sufficient space and equipment to perform maintenance activities safely and efficiently. Maintenance facilities must be clean and orderly.
(Second bullet) In addition to the special equipment essential to maintenance, the plant management provide special equipment where this could significantly reduce exposure or enhance safety and also provide adequate training in its use.
(Third bullet) Comprehensive programmes must optimize safe and reliable performance of plant systems and components over the lifetime of the plant. They are established for in service inspection, plant ageing and predictive, preventive and corrective maintenance.
(Fourth bullet) Preventive maintenance (PM) minimizes the potential for breakdown (corrective maintenance) of important equipment by the early detection and correction of equipment degradation. PM activities must be scheduled and carried out according to a defined programme.

## Slide 48: Maintenance
In-service inspection → examination of systems and components for possible deterioration;
Procedures, records and histories
Maintenance procedures and other work-related documents must:
  identify preconditions and precautions,
  provide clear instructions,
Instructions:
  point out the risk impact of the work, and
  identify the countermeasures and specify post maintenance testing.
Notes: (First bullet) The in-service inspection programme must be established to examine systems and components of the plant for possible deterioration. On this basis we can evaluate whether they are acceptable for continued safe operation of the plant or whether remedial measures must be taken. In service inspection programme is implemented in accordance with plant policy, regulating requirements and OLCs.
(Second bullet) Maintenance procedures and other work-related documents must identify preconditions, precautions, provide clear instructions for work to be done and must be used to ensure that maintenance is performed in accordance with the maintenance strategy, policies and programmes.
(Third bullet) Maintenance instructions issued to craftsmen must be compiled in accordance with quality assurance requirements. Then they must point out the risk impact of the work on nuclear and personnel safety and identify the countermeasures to be taken and specify post maintenance/modification testing required. Maintenance history must be used to support maintenance activities, upgrade maintenance programmes, optimize equipment performance and improve equipment reliability. Appropriate arrangements are made for orderly collection and analysis of records and production of reports on maintenance activities. Maintenance history records must be easily retrievable for reference or analysis.

## Slide 49: Maintenance
Conduct of maintenance work
Maintenance is conducted in a safe and efficient manner
Work is performed in accordance with policies and procedures
Personnel must be attentive to identifying plant deficiencies and responsive
Work control
Work control ensures that work activities are:
  → properly identified, prioritized, authorized, scheduled and carried out;
Notes: (First bullet) Maintenance must be conducted in a safe and efficient manner to support plant operation. Personnel must exhibit competence and professionalism, which result in quality workmanship when performing assigned tasks. Personnel must demonstrate also a questioning culture before, during and after the work is completed. Programmes and documentation support this culture.
(Second bullet) Managers and supervisors must routinely observe maintenance activities to ensure adherence to station policies and procedures.
(Third bullet) Maintenance personnel must be attentive to identifying plant deficiencies and responsive to correcting them with the goal of maintaining reliability and availability of equipment and systems.
(Fourth bullet) A comprehensive work planning and control system that considers defence in depth must be used to ensure that work activities are properly identified, prioritized, authorized, scheduled and carried out in accordance with appropriate procedures and completed in a timely manner.

## Slide 50: Maintenance
Effective operational feedback system and a systematic analysis;
Work scheduling must allocate parts, materials, resources and expertise at the appropriate time;
Spare parts and materials
Necessary parts and materials are made available and are suitable for use when needed.
Outage management
Safe and effective implementation and control of activities;
Outage planning is a continuing process;
Notes: (First bullet) The work control process must contain an effective operational feedback system and a systematic analysis of root causes of rework or repetitive failures.
(Second bullet) Work scheduling must allocate parts, materials, resources and expertise at the appropriate time for completion of the preventive and corrective programmes and make provisions for adequate post-maintenance testing.
(Third bullet) Materials management must ensure that necessary parts and materials, meeting established quality or design requirements, are made available and are suitable for use when needed throughout the lifetime of the plant.
(Fourth bullet) Outage management organization and administration must ensure the safe and effective implementation and control of maintenance activities during planned and forced outages. Outage planning and performance must take into consideration safety, quality and schedule in this order.
(Fifth bullet) Outage planning is a continuing process involving past, next scheduled and future outages. Milestones are determined and used to track pre-outage work. Planning must be completed as far in advance as possible as circumstances may cause the outage to begin earlier than intended.

## Slide 51: Technical support (TS)
TS covers all on-site activities of the technical and engineering groups involved in (e.g.):
  surveillance programme,
  plant performance monitoring,
  plant modifications,
  reactor engineering,
  fuel handling, and
Organization and functions
Goals and objectives → written and defined
  within the framework of plant policies and goals;
Notes: (First bullet) Technical support (TS) covers all on-site activities of the technical and engineering groups involved in surveillance testing, plant performance monitoring, plant modifications, reactor engineering, fuel handling, and application of plant process computers. The integration of technical support with its specialist functions into the plant organization is important in order to support and ensure the safe operation of the nuclear power plant.
(Second bullet) The goals and objectives of TS must be written and defined within the framework of plant policies and goals and be well understood by all personnel.
(Additional text) In those it must be clear that nuclear safety has an overriding priority. Performance indicators must be established that encourages these expectations and standards and are reported in periodic assessments.
(Third bullet) Good coordination between the TS, Operations and Maintenance groups is of utmost importance.
(Additional text) The organization and administration of the technical support ensures effective implementation and control of technical support activities. Effective implementation of the various technical support functions can be accomplished by having a separate section that is responsible for all such activities or by having various in-plant and off-site sections providing different support. The interface between TS and other plant on-site and off-site groups must be clearly specified.

## Slide 52: Technical support (TS)
Surveillance programme
Comprehensive and adequately documented surveillance programme → confirm provisions for safe operation and safety margins;
Verifies systems and components → ready to operate and perform their safety functions;
  Such programme → detect ageing trends;
Detect and correct any anomalous condition;
Notes: (First bullet) A comprehensive and adequately documented surveillance programme must be established and implemented to confirm that provisions for safe operation, which were made in the design and checked during construction and commissioning, continue to exist during the life of the plant. At the same time, the programme confirms that safety margins are adequate and provide a high tolerance for anticipated operational occurrences, errors and malfunctions.
(Second bullet) A surveillance test programme must verify that the plant systems and components relevant to safety are continuously ready to operate and are able to perform their safety functions as designed. Such a surveillance test programme must also detect ageing trends to prevent potential long term degradation.
(Third bullet) In addition a surveillance programme can detect and correct any anomalous condition before it significantly affects safety.
(Additional text) The concern of the surveillance programme is:
failures,
deficiencies, and
also trends and analyses.

## Slide 53: Technical support (TS)
Plant modification system
Programme encompass changes of:
  structures,
  systems,
  components and process software of power plant,
  operational limits and conditions,
  instructions and procedures
The design authority:
  review,
  verify and
  approve (or reject) design changes.
Notes: (First bullet) An overall plant modification programme encompass all intended changes of:
structures,
systems,
components and process software of power plant,
operational limits and conditions,
instructions and procedures.
(Second bullet) The design authority, or a responsible designer in its assigned area, must review, verify and approve (or reject) design changes to the plant.
(Additional text) Design changes include field changes, modifications and the acceptance of non-conforming items for repair or use without modification.
A plant modification programme for permanent and temporary modifications is established to ensure proper design, review, control, implementation and documentation of plant design changes in a timely manner. All changes requested are reviewed, controlled, installed, tested and documented according to plant safety rules and procedures. The plant safety level after a modification must be within the design basis for the plant.

## Slide 54: Technical support (TS)
Programme is integrated in to the overall plant configuration management system
Reactor core management (reactor engineering)
Safe and optimum operation of the reactor core
  maximum effort → fuel integrity;
Numerical methods and techniques → reactor behaviour;
Surveillance activities → early detection of any deterioration;
Handling of fuel and core components
Programme provides measures to prevent:
  damage of the nuclear fuel,
  inadvertent criticality, and
  loss of appropriate cooling;
Notes: (First bullet) The plant modification programme is integrated in to the overall plant configuration management system that identifies documented design requirements, ensures the design is properly implemented, and controls plant changes throughout the life of the plant.
(Second bullet) Reactor core management ensures the safe and optimum operation of the reactor core without compromising any OLCs based on design, safety or nuclear fuel limits.
Maximum effort and priority is assigned to maintaining fuel integrity.
(Additional text) The core management programme must also provide tools to control and ensure that only approved fuel is loaded into the core.
(Third bullet) Core management programme includes appropriate numerical methods and techniques to predict reactor behaviour during operation so as to ensure that the reactor will be operated within OLCs.
(Fourth bullet) A core management programme also includes the surveillance activities for the early detection of any deterioration that could result in an unsafe condition in the reactor core.
(Fifth bullet) The handling programme for fuel and other core components must provide measures to prevent damage to the nuclear fuel and to prevent inadvertent criticality and loss of appropriate cooling when fuel assemblies are being transported, stored or manipulated.

## Slide 55: Technical support (TS)
  Comprehensive fuel handling programme includes:
  receipt,
  transfer,
  inspection, and
  storage of nuclear fuel.
  Computer based systems important to safety
  Established and implemented to support and verify the safe operation of the plant;
Notes: (First bullet) The comprehensive fuel handling programme must include receipt, transfer, inspection and storage of nuclear fuel.
(Additional text) Fuel handling planning accomplishes fuel loading and unloading safely in accordance with a core management programme as well as safe storage, handling and preparation for dispatch of the irradiated fuel.
(Second bullet) Each core component is adequately identified and a record is kept:
of its core location,
orientation within the core,
out of core storage position,
and other pertinent information.
(Third bullet) A programme for utilization of computer based systems is established and implemented to support and verify the safe operation of the plant.
(Fourth bullet) Utilization of computer based systems may vary greatly between different plants.
The programme for utilization should therefore clearly define the categorization of the applications in terms of their safety significance.

## Slide 56: Operational experience feedback
Operational experience (OE) programme is characterized by the following features:
  Management aligns the organization;
  Report → in a timely manner;
  Sources → considered → to learn a lessons;
  Information → screened;
  Analysis → performed on appropriate events;
  Corrective actions → defined, prioritized, scheduled and followed up;
Notes: (First bullet) A well-implemented operational experience (OE) programme is characterized by the following features:
Management aligns the organization to effectively implement the OE programme in order that plant safety and reliability are improved.
OE is reported in a timely manner to reduce the potential for recurring events in-house and in the industry.
Sources of OE are considered in the OE programme to improve plant safety and reliability from the lessons learned.
OE information is appropriately screened to select and prioritize those items requiring further investigation.
Analysis is performed on appropriate events, depending of their severity or frequency, to ensure root causes and corrective actions are identified.
Corrective actions are defined, prioritized, scheduled and followed up to ensure effective implementation and effective improvement of plant safety and reliability.
OE information is used throughout the plant to effectively improve plant safety and reliability.
OE information is analysed and trended, and the results are used to improve plant safety and reliability.
Assessments and indicators are effectively used to review and monitor the plant performance and the effectiveness of OE programme.

## Slide 57: Operational experience feedback
  Reporting of operating experience
What can be reported:
  significant events, minor events, low level events,
  near misses and potential problems,
  equipment failures,
  human performance problems, …..
  Sources of operating experience
Organizations (IAEA, NEA, WANO,…) and publications (IRS, SER,…)
Sources of in house OE include areas such as:
  significant events, low level events and near misses,…
Notes: (First bullet) Significant events, minor events, low level events, near misses and potential problems are identified and reported, including equipment failures, human performance problems, procedure deficiencies and documentation inconsistencies.
(Second bullet) Sources of industry operating information are identified, access to these sources are formally established and systematically screened. These sources include organizations (IAEA, NEA, WANO, INPO, National Regulatory Body, Owners Groups, Vendors and Manufacturers, Engineering designer etc.) and publications (IRS, SER, SOER; National Regulatory Body Generic Letters, Bulletins, Notices; Vendors, Manufacturers and Engineering designer problem information; Utilities and Industry event reports). Sources of OE include good practices as a source of improvement.
(Third bullet) Sources of in house OE are identified, information from and access to these sources are formally established and systematically screened. These sources include areas such as:
Significant events.
Low level events and near misses.
Quality reports, reports and data from operation activities.
Maintenance testing and in-service inspection.
Surveillance reports.
Results from plant specific safety assessments.
Training feedback.
No-blame reporting programme.
Performance indicators.

## Slide 58: Operational experience feedback
  Screening of operating experience information
Screening → select and prioritize the information
  screening criteria → established and defined;
Screening → systematic and timely manner;
  Analysis
Analysis is performed on the selected events in accordance to their level of:
Rigorous investigation with full root cause analysis;
Notes: (First bullet) OE information is appropriately screened, to select and prioritize the information for further investigation.
Screening criteria for in-house and industry OE are clearly established and the criteria for the subsequent level of investigation and distribution are defined.
(Second bullet) The screening is performed in a systematic and timely manner.
(Third bullet) Analysis is performed on the selected events in accordance to their level of safety significance, severity and frequency to ensure that root causes and corrective actions are identified.
(Fourth bullet) For significant in-house events, including scrams, plant transients and important human performance and equipment problems, a rigorous investigation with full root cause analysis is performed, including causal factors, generic implications, and discrepancies between expected and actual plant responses and or personnel actions.Personnel who have appropriate knowledge, experience and skills perform investigations/analysis. Event participants are involved in developing and implementing corrective actions, as necessary.

## Slide 59: Operational experience feedback
Investigation → initiated promptly;
  Corrective actions
Results of OE reviews and analysis → define corrective actions;
  Fundamental causes of problems;
  Priority, schedule for implementation and effective implementation;
  Tracking → verifying final implementation;
  Use of operating experience
Use of OE in personnel work activities
  to remind the personnel
  → to enhance alertness and to reduce risks;
Notes: (First bullet) Investigation of events is initiated promptly to preserve information and physical evidence and to interview participants while the events are fresh in their memories. Investigations are carried out in a timely manner.
(Second bullet) The results of OE reviews and analysis are used to identify corrective actions.
Corrective actions address fundamental causes of problems, rather than the symptoms to avoid recurrence of events.
Corrective actions are prioritised, scheduled for implementation, and effectively implemented.
Corrective actions are tracked for completion to verify their final implementation.
(Third bullet) Use of OE in personnel work activities (i.e. pre-job briefings and pre-evolution briefings, work planning, shift briefings etc.) is carried out to remind the personnel involved of lessons learned and precautions from OE, to enhance the personnel alertness and to reduce risks.

## Slide 60: Operational experience feedback
  Database and trending of operating experience
Databases are established to facilitate an integral view and analysis of OE from the point of view of:
  organizational aspects,
  human factors,
  equipment failures,
  work management, and
  maintenance deviation reports
  Assessments and indicators of operating experience
Self-assessments and independent evaluation → periodically
  effectiveness and effective use;
Notes: (First bullet) Databases related to events, deficiencies, anomalies, deviations, are established to facilitate an integral view and analysis of OE from the point of view of organizational aspects, human factors, equipment failures, work management and maintenance deviation reports.
(Second bullet) Self-assessments and independent evaluation are periodically performed to determine the effectiveness of the OE programme and the effective use of OE information.

## Slide 61: Operational experience feedback
Examples of indicators (safety performance):
  recurrent safety systems unavailability,
  industrial safety events,
  reactor scrams, etc.
Examples of indicators (effectiveness of OE programme):
  average time for initial screening of OE documents,
  number and age of reports awaiting evaluation,
  number and age of corrective actions awaiting implementation,
Notes: (First bullet) Indicators are used to monitor the safety performance of the plant. The trends of indicators are evaluated during self-assessment. Examples of these indicators are: recurrent safety systems unavailability, industrial safety events, reactor scrams, volume of low-level waste, radiation doses.
(Second bullet) Indicators are used to track the effectiveness of OE programme. Examples of these indicators are: average time for initial screening of OE documents, number and age of reports awaiting evaluation, number and age of corrective actions awaiting implementation, recurrent events and root causes, reworks, ratio of events detected through surveillance and quality programmes versus operational failures or degradation in service.

## Slide 62: Radiation protection
The radiation protection (RP) regime
  doses due to exposure to ionizing radiation → kept below prescribed limits and ALARA
Controls for RP
  to protecting workers and members of the public,
  Organization and functions
RP goals and objectives → defined in the safety policies;
Programme → meet the requirements of the International Basic Safety Standards for Protection against Ionizing Radiation and for the Safety of Radiation Sources (BSS);
Notes: (First bullet) The radiation protection (RP) regime established and implemented by operating organization at nuclear power plant ensures that in all operational states doses due to exposure to ionizing radiation in the plant or due to any planned releases of radioactive material from the plant are kept below prescribed limits and ALARA.
(Second bullet) Controls for RP during operation of the plant, including the management of radioactive effluents and waste arising in the plant, are directed not only to protecting workers and members of the public from radiation exposure, but also to preventing or reducing potential exposures and mitigating their potential consequences.
(Third bullet) The RP goals and objectives are clearly defined in the safety policies of the operating organization and communicated to the personnel and the management of the power plant.
To achieve these goals and objectives well-structured RP programme is established and implemented.
(Fourth bullet) The programme is documented in the plant policies and procedures and must meet the requirements of the International Basic Safety Standards for Protection against Ionizing Radiation and for the Safety of Radiation Sources (BSS).
(Additional text) The management ensures that the RP policies and procedures are well understood by the plant's personnel. The RP programme is clearly oriented to the achievement of a level of performance in RP that is well above minimum regulatory requirements.

## Slide 63: Radiation protection
Independence and resources → enforce and give advice:
  regulations,
  standards and procedures, and
  safe working practices;
An independent RP group also known as the Health Physics Group;
The operating organization verifies the RP programme and undertakes corrective actions if necessary, by means of:
  surveillance,
  inspections and
  audits
Notes: (First bullet) The RP function in the operating organization has sufficient independence and resources to enforce and give advice on RP regulations, standards and procedures and safe working practices.
(Second bullet) An independent RP group (in some countries known as the Health Physics Group) is established, which has the authority to enforce RP regulations, standards, procedures, safe working practices and appropriate health physics surveillance.
(Third bullet) The operating organization verifies, by means of surveillance, inspections and audits, that the RP programme is being correctly implemented and that its objectives are being met, and will undertake corrective actions if necessary.
(Additional text) The programme is reviewed and updated in the light of experience.

## Slide 64: Radiation protection
  Radiation work control
Exposure (external and internal) → ALARA
  individual and collective doses;
Responsibility for optimizing occupational exposure
  management and RP group;
  Control of occupational exposure
Dose limits recommended by ICRP and IAEA → not exceeded;
A hierarchy of control measures → optimization:
Notes: (First bullet) The exposure from the sources of external and internal radiation at nuclear power plant is reduced to such dose levels that are as low as reasonably achievable (ALARA).
This principle applies both to individual and to collective doses.
(Second bullet) The responsibility for optimizing occupational exposure rests both with management of different levels and with the RP group.
(Third bullet) The occupational exposure at the power plant is so controlled that the dose limits recommended by ICRP and IAEA are not exceeded.
(Fourth bullet) A hierarchy of control measures are taken into account in optimization. Firstly, removal or reduction in intensity of the source of radiation must be considered. Only after this has been done the uses of engineering means to reduce doses be considered. The use of systems of work are then considered and, lastly, the use of personal protective equipment.

## Slide 65: Radiation protection
Dose monitoring of individuals and management of dose records:
  requirements → regulatory authority, and
  recommendations → ICRP and IAEA;
  Radiation protection instrumentation, protective clothing and facilities
For normal and emergency situations must be provided:
  radiological instrumentation,
  protective clothing,
  facilities, and
  equipment;
Notes: (First bullet) Dose monitoring of individuals and management of dose records comply with requirements established by the regulatory authority and are consistent with the applicable recommendations of ICRP and IAEA.
(Second bullet) In situations where significant concentrations of airborne activity are anticipated, appropriate internal dosimetry is available, including whole body counters.
(Third bullet) Adequate radiological instrumentation, protective clothing, facilities and equipment both for normal and emergency situations are provided as part of the RP programme.

## Slide 66: Radiation protection
  Radioactive waste management and discharges
Generation of radioactive waste → minimum practicable
Programme
  safely manage radioactive waste;
  monitor and control discharges;
Authorized discharge limits → in the OLCs;
  Radiation protection support during emergencies
Programme for RP support during emergencies
  serve the purpose of optimizing worker exposure and the general public;
Notes: (First bullet) The generation of radioactive waste is kept to the minimum practicable in terms of both activity and volume, by appropriate operating practices.
(Second bullet) The operating organization establishes and implements a programme to safely manage radioactive waste and monitor and control discharges of radioactive effluents.
(Third bullet) Any authorized discharge limits are included in the OLCs. Radioactive waste and effluent releases are documented as required and an environmental monitoring programme is in place.
(Fourth bullet) The programme for RP support during emergencies is comprehensive and serve the purpose of optimizing both worker exposure and the exposure of the general public to the extent consistent with emergency conditions.

## Slide 67: Chemistry
Chemistry → activities of chemical treatment
  maintaining the integrity of the barriers;
  limiting all kinds of corrosion processes;
Chemical treatment
  effects on the out-of-core radiation fields → influence on radiation doses;
  Organization and functions
The operating organization establishes chemistry policy → states the goals and objectives,
Notes: (First bullet) Chemistry involves activities of chemical treatment to maintain the integrity of the barriers retaining radioactivity, including fuel cladding and primary circuit. The chemistry activities have a direct impact in limiting all kinds of corrosion processes causing either direct breach of safety barriers or weakening of them so that failure could occur during a transient.
(Second bullet) In addition the chemical treatment includes consideration of its effects on the out-of-core radiation fields that in turn influence radiation doses to which the workers are exposed.
(Third bullet) The operating organization establishes chemistry policy for nuclear power plants. The policy states the goals and objectives of chemistry programme and the expectations of the management concerning the implementation of this programme at the plant. Performance indicators are established that encourages these expectations and are reported in periodic assessments.

## Slide 68: Chemistry
The organization of the chemistry group contributes to:
  safe operation,
  define responsibilities, and
Group's expectations, goals and objectives
  derived → the plant policies and objectives,
  Chemistry control in plant systems
A comprehensive chemistry control programme
  Implemented → procedures;
Notes: (First bullet) A specific chemistry group is established at the plant to implement chemistry control programme. The organization of the chemistry group contributes to safe operation, define responsibilities and establish lines of communication inside and outside the group. (Additional text) The position of this group in the organization reflects its relevance. The interfaces between the chemistry group and other groups are clearly specified especially as regards to allocation of authorities. The chemistry group is consulted when issues affecting chemistry are being addressed.
(Second bullet) The chemistry group's expectations, goals and objectives are derived from the plant policies and objectives and defined in line with vendor recommendations and international good practice. They must be well understood by the chemistry personnel.
(Third bullet) The plant must have established and implemented a comprehensive chemistry control programme. This programme is implemented by clear procedures and monitored by adequate performance indicators.
(Additional text) The concerned plant staff has a good understanding of the programme, procedures and indicators.

## Slide 69: Chemistry
  Chemistry surveillance programme
Programme includes:
  monitoring, sampling, and
  trending of chemistry and radiochemistry parameters;
Programme reflects chemistry specifications for all phases of plant operation
  Chemistry operational history
Results of analysis and investigations → trended, evaluated and reported;
  Records → available and retrievable;
Notes: (First bullet) The chemistry surveillance programme includes the monitoring, sampling and trending of chemistry and radiochemistry parameters at specified frequencies to ensure the timely detection and correction of abnormal or unacceptable trends and conditions.
(Second bullet) The chemistry surveillance programme reflects chemistry specifications for all phases of plant operation including shutdown periods and when systems are taken out of operation for prolonged periods.
(Third bullet) The results of analysis and investigations must be adequately trended, evaluated and reported. Records are available and easily retrievable. Lessons and experiences from previous events and history, including from other plants are considered in the plant chemistry.

## Slide 70: Chemistry
  Laboratories, equipment and instruments
Laboratories → adequate space, supplies and equipment;
Sampling systems → reliable and safe for use
  including post-accident;
Instruments for performing the analysis → available and calibrated;
  Quality control of operational chemicals and other substances
Purity and nature of chemicals → specified and controlled
Notes: (First bullet) The laboratories have adequate space, supplies and equipment.
(Second bullet) The sampling systems are reliable and safe for use, including post-accident sampling systems.
(Third bullet) Necessary and adequate instruments for performing the analysis are available and calibrated.
(Fourth bullet) The purity and nature of chemicals and other substances, which might have an impact on safety, related systems are specified and controlled.
Before being used the specified values are verified by certification or by chemical analysis.

## Slide 71: Emergency planning and preparedness
Emergency preparedness → capability to take actions that will effectively mitigate the consequences:
  human health and safety, quality of life, property and the environment;
Practical goals of emergency response:
  To regain control of the situation;
  To prevent or mitigate consequences at the site;
  To prevent the occurrence of deterministic health effects;…..
Notes: (First bullet) Emergency preparedness is the capability to take actions that will effectively mitigate the consequences of an emergency for human health and safety, quality of life, property and the environment.
(Additional text) This section refers to emergency planning and preparedness both on-site of the nuclear plant (operator responsibility) and off-site area (mostly local and state authorities responsibility).
(Second bullet) The practical goals of emergency response in a nuclear or radiological emergency are:
To regain control of the situation;
To prevent or mitigate consequences at the site;
To prevent the occurrence of deterministic health effects in workers and the public;
To render first aid and manage the treatment of radiation injuries;
To prevent, to the extent practicable, the occurrence of stochastic health effects in the population;
To prevent, to the extent practicable, the occurrence of adverse non-radiological effects on individuals and among the population;
To protect, to the extent practicable, the environment and property;
To prepare, to the extent practicable, for the resumption of normal social and economic activity.

## Slide 72: Emergency planning and preparedness
An emergency preparedness programme is necessary that includes national, local, and on-site response organizations
  Emergency programme
Arrangements are in place to provide reasonable assurance of an effective response in the case of any nuclear or radiological emergency.
An effective administrative framework is available for the:
  planning,
  implementation,
  co-ordination, and control of emergency preparedness activities.
Notes: (First bullet) In a consolidated approach, the elements to be evaluated may be addressed by the operator, the local authorities or the national authorities, or by a combination thereof, so long as the arrangements are well coordinated. Weaknesses at one level could be compensated at another.
(Second bullet) Arrangements including clearly assigned authorities and responsibilities, organization, coordination, personnel, plans, procedures, facilities, equipment and training are in place to provide reasonable assurance of an effective response in the case of any nuclear or radiological emergency at the site that meets the practical goals of emergency response.
(Third bullet) An effective administrative framework is available for the planning, implementation, co-ordination and control of emergency preparedness activities. This framework is well documented, defining responsibilities and authorities and appropriately consider the requirements of the regulatory authority.
(Fourth bullet) The operating organisation policy ensures that all emergency preparedness activities at the plant are properly organized and are integrated with those of the operating organisation's headquarters organization, the relevant emergency services, the local and national authorities, with due consideration to interface implications. Authorities and responsibilities are well established and clear among all organizations involved.

## Slide 73: Emergency planning and preparedness
A close and co-operative relationship is maintained between on- and off-site response organizations.
The response organizations periodically conduct a review
  Emergency plans and organization
Approved emergency plans clearly allocate responsibilities and provide a basis for:
  development of procedures,
  training, and
  other arrangements for a coordinated response;
Notes: (Second bullet) The response organizations periodically conduct a review in order to ensure that all the events (including those of very low probability) that could necessitate an emergency response are addressed by the emergency arrangements. This includes a review and appropriate revision of the emergency arrangements before any revisions to existing operations or new operations are commenced on the site or nearby that may result in events warranting an emergency response.
(Third bullet) Approved emergency plans clearly allocate responsibilities and provide a basis for development of procedures, training and other arrangements that provide for a coordinated response by the operating organization and other authorities.
(Fourth bullet) The emergency plans include arrangements for emergencies involving a combination of non-nuclear and nuclear hazards and response of conventional response organizations such as law enforcement.

## Slide 74: Emergency planning and preparedness
  Emergency procedures
Procedures and analytical tools are:
  available,
  validated, and
  provide detailed guidance;
  Emergency equipment and resources
Where is needed an adequate emergency systems are available:
  emergency equipment and resources,
  communication systems, ……..
Notes: (First bullet) Procedures and analytical tools are available, validated and provide detailed guidance for the rapid and effective implementation of the response functions.
(Second bullet) Facilities are provided for adequate on-site and off-site emergency response with appropriate communications and equipment that can be brought into operation without delay in the event of an emergency.
(Third bullet) Adequate emergency equipment and resources, communication systems, documentation (such as procedures, checklists, telephone numbers, and manuals) are available where needed to properly initiate and support the emergency response actions. Necessary data transfer and communication is also available.

## Slide 75: Emergency planning and preparedness
  Training, drills and exercises
Training programme is provided for developing and maintaining the necessary:
  knowledge,
  skills, and
  physical ability;
A programme of periodic drills and exercises
  to reinforce the training and assess the effectiveness of the emergency response capability;
Notes: (First bullet) A comprehensive, documented training programme is provided for developing and maintaining the necessary knowledge, skills and physical ability required for all persons having duties under the emergency plans, to enable them to respond correctly and efficiently in the event of an emergency.
(Second bullet) A programme of periodic drills and exercises is set up to reinforce the training and assess the effectiveness of the emergency response capability.

## Slide 76: Commissioning
Commissioning is the process of fine-tuning and testing of the power plant before operation
Commissioning also includes testing prior and subsequent to fuel loading
the best scenario to prepare personnel and procedures
results are an important part of the licensing process of the plant
responsibility for the plant is eventually transferred to the operating organization
Notes: (First bullet) Commissioning is the process during which plant components, systems and structures having been constructed, are tested and placed in operation with the objective of verifying that these are in accordance with the design assumptions. This process continues until the plant is at full power and required testing at this power level has been conducted.
(Second bullet) Commissioning also includes testing prior and subsequent to fuel loading. It is therefore essential to safety that the commissioning programme and individual system testing be designed in such a way that those design assumptions can be verified and quality can be assured throughout the commissioning process.
(Third bullet) The commissioning process is the best scenario to prepare personnel and procedures for the normal operation of the plant. Operating personnel in all disciplines are involved as much as possible in commissioning activities and the operating procedures are validated to the practicable extent with the participation of future operating staff.
(Fourth bullet) The commissioning programme and results are an important part of the licensing process of the plant. Clear and well defined responsibilities and requirements for the operating, commissioning and regulatory organizations are essential to satisfy in a timely manner the licensing requirements for the plant.
(Fifth bullet) The responsibility for the plant is eventually transferred to the operating organization. This could be done gradually or in specified stages. Quality and comprehensiveness of this handover is necessary to ensure an adequate history and that the plant meets the design intent.

## Slide 77: Commissioning
  Organization and functions
Responsibility for commissioning:
  a contractor,
  the construction organization,
  or the operating organization
Fuel loaded → responsibility rests with the license holder;
Operating personnel and plant technical staff
  involved in the commissioning process;
The responsibility of the regulatory authority
  clearly defined and well understood;
Notes: (First bullet) Responsibility for commissioning may rest with a contractor, the construction organization or the operating organization.
(Second bullet) Nevertheless, since the time of fuel load the responsibility for nuclear safety must rests with the license holder, usually the operating organization.
(Third bullet) A sufficient number of qualified personnel must be available during all stages of commissioning. Operating personnel and plant technical staff is involved in the commissioning process to the extent necessary for ensuring proper preparation of the operational phase.
(Fourth bullet) The responsibility of the regulatory authority in the commissioning programme is clearly defined and well understood by the commissioning organization and operating organization.

## Slide 78: Commissioning
  Commissioning programme
Commissioning programme
  management tool and
  regulatory body tool;
Objectives:
  Tests → conducted;
  Means of identifying hold points;
  Personnel trained and procedures validated;
Notes: (First bullet) The commissioning programme is a management tool which allows those responsible to satisfy themselves that the scope and sequence of the commissioning process is adequate for the purpose and against which it may be controlled.
It also provides a reference against which the regulator may monitor and approve the process and allocation of safety responsibilities at different stages during the commissioning process from fuel arrival at the plant to full power operation.
(Second bullet) A good commissioning programme is structured to ensure that the following objectives are met:
All the tests necessary to demonstrate that the installed plant satisfy the design intent are conducted.
The tests are performed in a logical sequence.
The programme provides a means of identifying hold points in the commissioning process.
Operation personnel trained and procedures validated. Commissioning activities are scheduled to align them with critical path activities and take into consideration all organizations involved. The schedule will ensure that tests are performed in a logical sequence.

## Slide 79: Commissioning
  Training in commissioning
Commissioning → quick transition from construction to operation;
  Significant changes in methods and disciplines;
  Training and assessment of the commissioning personnel → established, understood and conducted in adequate time;
  Preparation and approval of test procedures
Test procedures
  define → commissioning of equipment or system;
  form → core of the commissioning process;
Notes: (First bullet) The commissioning of a NPP is a relatively quick transition from construction to operation. Throughout this process, significant changes in methods and disciplines occur. For this reason training and assessment of the commissioning personnel is well established, understood and conducted in adequate time in order to meet the quality requirements of the commissioning programme at any time.
(Second bullet) Training must be well staffed with experienced personnel in all subjects and the training programme contains specific commissioning aspects. Designers, vendors, main contractors and operations are encouraged to participate in the training programme because of the close interaction during this phase.
(Third bullet) The test procedures define in detail how each equipment or system will be commissioned and thus form the core of the commissioning process.

## Slide 80: Commissioning
  Interface with construction
Responsibilities of the construction group in relation to the commissioning process;
Maintenance activities → follow operation QA standards during commissioning;
  Interface with engineering (designer)
Validation of the design
  Result → identifies weaknesses in design;
All design changes → approved and conform to the design;
  Evaluation of the proposed design changes;
Notes: (First bullet) The responsibilities of the construction group in relation to the commissioning process include the following:
To ensure that the installation of structures, systems and components has been completed in accordance with design requirements and specifications.
To make suitable arrangements for surveillance and maintenance to prevent deterioration after the completion of installation and before the handover.
To issue certificates of completion of installation giving the necessary assurances to the commissioning group.
To provide, for use as baseline data, as-built documentation of installation and test certificates, highlighting design changes and concessions.
To transfer the installed systems to the commissioning group using a system of documents such as transfer certificates.
To correct deficiencies in installation detected in commissioning.
(Second bullet) The quality of maintenance activities must follow operation QA standards during commissioning, especially from core loading where the license holder would be responsible to ensure this.
(Third bullet) During the commissioning process a thorough validation of the design of the plant is carried out.
As a result, a comprehensive programme to identify weaknesses in design and equipment deficiencies is established.
(Fourth bullet) Mechanisms exist at the plant to confirm that all design changes are approved and conform to the design intent.
This is achieved by thoroughly evaluating the proposed design changes prior to their implementation by all organizations involved and by testing the system or equipment after implementation of the changes.

## Slide 81: Commissioning
  Initial fuel loading
Initial fuel load → first time for potential criticality
First fuel assembly inserted into the reactor core
  responsibility for nuclear safety rests with the license holder;
  Plant handover
Transfer of responsibilities;
  Includes systems, equipment, structures and documentation and may include personnel;
Systems transfer
  after the non-nuclear tests and before the pre-nuclear tests;
Notes: (First bullet) Initial fuel load is of great significance because it is the first time that the fuel is brought into a potential critical configuration.
This potential for criticality carries with it the potential for radiation hazards, contamination and even nuclear emergencies.
(Second bullet) When the first fuel assembly is inserted into the reactor core, the responsibility for nuclear safety at the plant rests with the license holder or his designee, usually the plant manager.
(Third bullet) Plant handover is the transfer of responsibilities for the plant.
This transfer is comprehensive and includes systems, equipment, structures and documentation and may include personnel.
(Fourth bullet) Systems are transferred gradually to the operating organization as soon as the non-nuclear tests are performed and approved. In this way the operating organization can carry out the inspection in a thorough manner prior to acceptance. Systems are also transferred before the pre-nuclear tests are performed or approved, with exclusive operating responsibilities.
(Fifth bullet) The transfer of documentation is a key feature in the handover process.
(Additional text)This is done in system packages and take place over a reasonable period of time in order for the plant to be able to make a comprehensive review of every package.

## Slide 82: Summary
Operational safety is a very broad topic that covers every aspect of the operation of nuclear facilities
Objective of this module is to gather together and briefly summarize in one place the various documents issued under the auspices of the IAEA dealing with operational safety and operational experience feedback
In view of the long term importance of nuclear safety, the capture and preservation of operating experience information is of utmost importance to facilitate the transfer of knowledge and skills to the next generation
Notes: In view of the long term importance of nuclear safety, the capture and preservation of operating experience information is of utmost importance to facilitate the transfer of knowledge and skills to the next generation. This requires a new and well organized database where the information of interest can be searched by properly arranged topics.

## Slide 83: Key points
The prime responsibility for safety shall be assigned to the operating organization of the nuclear power plant
Prime responsibility shall cover all the activities relating to the operation directly and indirectly
Effective OEF is useful not only to operators and regulators, but also to designers and vendors of nuclear facilities

## Slide 84: List of abbreviations
MOA: Management, organization and Administration
RP: Radiation Protection
ALARA: As Low as Reasonably Achievable

## Slide 85: References
INTERNATIONAL ATOMIC ENERGY AGENCY, Preparedness and Response for a Nuclear or Radiological Emergency, General Safety Requirements No. GSR Part 7, IAEA, Vienna, Austria (2015).
INTERNATIONAL ATOMIC ENERGY AGENCY, The Operating Organization for Nuclear Power Plants, Safety Guide NS‑G‑2.4, IAEA, Vienna, Austria (2001).
INTERNATIONAL ATOMIC ENERGY AGENCY, A System for Feedback of Experience from Events in Nuclear Installations, Safety Guide NS‑G‑2.11, IAEA, Vienna, Austria (2006).
INTERNATIONAL ATOMIC ENERGY AGENCY, Ageing Management for Nuclear Power Plants, Safety Guide NS‑G‑2.12, IAEA, Vienna, Austria (2009).
INTERNATIONAL ATOMIC ENERGY AGENCY, Fire Safety in Operation of Nuclear Power Plants, Safety Guide NS‑G‑2.1, IAEA, Vienna, Austria (2000).
INTERNATIONAL ATOMIC ENERGY AGENCY, Recruitment, Qualification and Training of Personnel for Nuclear Power Plants, Safety Standards Series No. NS‑G‑2.8, IAEA, Vienna, Austria (2002).
INTERNATIONAL ATOMIC ENERGY AGENCY, Commissioning for Nuclear Power Plants, Safety Standards Series No. SSG‑28, IAEA, Vienna, Austria (2013).
INTERNATIONAL ATOMIC ENERGY AGENCY, Commissioning of Research Reactors, Safety Guide NS‑G‑4.1, IAEA, Vienna, Austria (2006).

## Slide 86: References
INTERNATIONAL ATOMIC ENERGY AGENCY, Core Management and Fuel Handling for Nuclear Power Plants, Safety Guide NS‑G‑2.5, IAEA, Vienna, Austria (2002).
INTERNATIONAL ATOMIC ENERGY AGENCY, Conduct of Operations at Nuclear Power Plants, Safety Guide NS‑G‑2.14, IAEA, Vienna, Austria (2008).
INTERNATIONAL ATOMIC ENERGY AGENCY, Maintenance, Surveillance and In-service Inspection in Nuclear Power Plants, Safety Guide NS‑G‑2.6, IAEA, Vienna, Austria (2002).
INTERNATIONAL ATOMIC ENERGY AGENCY, Modifications to Nuclear Power Plants, Safety Guide NS‑G‑2.3, IAEA, Vienna, Austria (2001).
INTERNATIONAL ATOMIC ENERGY AGENCY, Radiation Protection and Radioactive Waste Management in the Operation of Nuclear Power Plants, Safety Standards Series No. NS‑G‑2.7, Vienna, Austria (2002).
INTERNATIONAL ATOMIC ENERGY AGENCY, Periodic Safety Reviews of Nuclear Power Plants, SSG‑25, Vienna, Austria (2013).
INTERNATIONAL ATOMIC ENERGY AGENCY, Decommissioning of Nuclear Power Plants and Research Reactors, Safety Guide WS‑G‑2.1, IAEA, Vienna, Austria (1999).

## Slide 87: References
INTERNATIONAL ATOMIC ENERGY AGENCY, Operational Limits and Conditions and Operating Procedures for Nuclear Power Plants, Safety Guide NS‑G‑2.2, IAEA, Vienna, Austria (2000).
INTERNATIONAL ATOMIC ENERGY AGENCY, Conduct of Operations at Nuclear Power Plants, Safety Guide NS‑G‑2.14, IAEA, Vienna, Austria (2008).
INTERNATIONAL ATOMIC ENERGY AGENCY, Safety of Nuclear Power Plants: Commissioning and Operation, Safety Requirements SSR‑2/2, IAEA, Vienna, Austria (2011).
INTERNATIONAL ATOMIC ENERGY AGENCY, The Management System for Nuclear Installations, Safety Guide GS‑G‑3.5, IAEA, Vienna, Austria (2009).
INTERNATIONAL ATOMIC ENERGY AGENCY, Fundamental Safety Principles, Safety Fundamentals No. SF‑1, IAEA, Vienna, Austria (2006).
INTERNATIONAL ATOMIC ENERGY AGENCY, Safety of Nuclear Power Plants: Design, Specific Safety Requirements SSR‑2/1, IAEA, Vienna, Austria (2012).
INTERNATIONAL ATOMIC ENERGY AGENCY, Operational Safety Performance Indicators for Nuclear Power Plants, IAEA‑TECDOC‑1141, Vienna (2000).

## Slide 88: References
INTERNATIONAL ATOMIC ENERGY AGENCY, Operations Manual for Incident and Emergency Communication, Emergency Preparedness and Response Series EPR‑IE Comm 2012, IAEA, Vienna (2012).
INTERNATIONAL ATOMIC ENERGY AGENCY, Chemistry Programme for Water Cooled Nuclear Power Plants, IAEA Safety Standards No. SSG‑13, IAEA, Vienna, Austria (2011).

## Slide 89: Discussion Questions
  What is importance of administrative procedures, rules and instructions in the nuclear power plant?
  Why it is important to integrate the technical support into the plant organization?
  List features that characterize a well-implemented operating experience programme.
  Please mention/names some sources of operating experience.
  What are objectives of a good commissioning programme?
Notes: Answer 1:
To ensure safe and effective methods of working and uniformity of performance, the nuclear power plant must have administrative procedures, rules and instructions which cover all aspects of plant operation and are applicable to all personnel on site.
Answer 2:
Technical support (TS) covers all on‑site activities of the technical and engineering groups involved in surveillance testing, plant performance monitoring, plant modifications, reactor engineering, fuel handling, and application of plant process computers. The integration of technical support with its specialist functions into the plant organization is important in order to support and ensure the safe operation of the nuclear power plant.
Answer 3:
A well‑ implemented operational experience (OE) programme is characterized by the following features:
Management ensures the organization effectively implements the OE programme in order that plant safety and reliability are improved.
OE is reported in a timely manner to reduce the potential for recurring events in‑house and in the industry.
Sources of OE are considered in the OE programme to improve plant safety and reliability from the lessons learned.
OE information is appropriately screened to select and prioritize those items requiring further investigation.
Analysis is performed of appropriate events, depending on their severity or frequency, to ensure root causes and corrective actions are identified.
Corrective actions are defined, prioritized, scheduled and followed up to ensure their effective implementation and the effective improvement of plant safety and reliability.
OE information is used throughout the plant to effectively improve plant safety and reliability.
OE information is analysed and trended, and the results are used to improve plant safety and reliability.
Assessments and indicators are effectively used to review and monitor plant performance and the effectiveness of the OE programme.
Answer 4:
These sources include organizations (IAEA, NEA, WANO, INPO, National Regulatory Body, Owners Groups, Vendors and Manufacturers, Engineering designer etc.) and publications (IRS, SER, SOER; National Regulatory Body Generic Letters, Bulletins, Notices; Vendors, Manufacturers and Engineering designer problem information; Utilities and Industry event reports). Sources of OE include good practices as a source of improvement.
Answer 5:
Commissioning is the process during which plant components, systems and structures, after construction, are tested and placed in operation with the objective of verifying that they are in accordance with the design assumptions. This process continues until the plant is at full power and the required testing at this power level has been conducted. In order to meet the expected performance criteria the plant is verified 'as built' and pre‑operational plant adjustments are made. Commissioning also includes testing prior and subsequent to fuel loading.

## Slide 90: Use this box for any additional message
Thank you!
Notes: Thank you!