## Slide 1: Unit 2: Functional and infrastructural elements for emergency preparedness and response
Name of Lecturer
Organization
Email address
Notes: Instructions for the Lecturer:
Unit 2 – on functional and infrastructural elements for preparedness and response for a nuclear or radiological emergency, with focus on nuclear emergencies (at facilities in EPC I and II)
Time allocated – 80 minutes, number of ‘active’ slides: 54 of 59
Last slide: 10 minutes discussions

## Slide 2: Learning objectives
To become familiar with the functional and infrastructural elements which have to be in place at all levels when building the EPR framework, the associated international requirements and practical aspects for implementation

## Slide 3: Contents
1. Functional elements for emergency preparedness and response
2. Infrastructural elements for emergency preparedness and response

## Slide 4: Introduction
Elements for sound preparedness and response for a nuclear or radiological emergency are divided into functional (response) elements and infrastructure (preparedness) elements
The functional elements described in this lecture address the functions that are essential for an effective response in a nuclear or radiological emergency in order to achieve the emergency response goals
An integrated set of infrastructural elements is to be established, for building adequate capabilities in support to the response functions
Notes: For each element, specific requirements are described in GSR Part 7.

## Slide 5
1. Functional elements for emergency preparedness and response

## Slide 6: Managing operations in an emergency
On-site emergency response promptly executed without impairing performance of normal operational safety functions
Off-site emergency response coordinated with on-site response (EPC I and II) and between all jurisdictions, response organizations, and countries that fall within PAZ or UPZ to provide mutual support
Appraise information on allocation of resources throughout emergency
Arrangements made for implementation of an Incident Command System (ICS) for response to any nuclear or radiological emergency

## Slide 7: Identifying, notifying and activating
For facilities in EPC I, II & III
  Ensure operators promptly determine appropriate emergency class or level of response
  Initiate on-site actions
  Notify and provide updated information to off-site notification point
  Promptly notify all appropriate off-site response organizations
  Which will initiate pre-planned and coordinated responses appropriate to emergency class

## Slide 8: Identifying, notifying and activating - cont’d
Initiate appropriate emergency response actions upon receipt of notification by another State or IAEA of actual or potential transnational emergency
In transnational emergency – notifying State informs directly or through IAEA those States that may be affected

## Slide 9: In practice
Emergency classification system must be in place
Off-site notification protocols and messages
Means to activate critical staff 24 hrs / 7 days
Means to notify other countries
First responders aware of indicators of presence of radiation or radioactive material
Medical doctors aware of symptoms that high dose of ionizing radiation can cause

## Slide 10: Taking mitigatory actions
Mitigatory actions refer to immediate actions to be taken on-site in order to:
prevent severe damage to fuel in the reactor core or spent fuel pool, so that preventing a large release of radioactive material into the environment
reduce the size of any release following damage to fuel
delay a large release of radioactive material following damage to fuel to allow protective actions to be taken
Notes: Mitigatory actions for a nuclear emergency refer to immediate actions to be taken on-site:
- To prevent severe damage to fuel in the reactor core or spent fuel pool and thus prevent a large release of radioactive material,
- To reduce the size of any release following damage to fuel, and
- To delay a large release of radioactive material following damage to fuel to allow protective actions to be taken most effectively on-site and off-site.

## Slide 11: Taking mitigatory actions – cont’d
Emergency operating procedures (EOP)
  To control transients such as Loss of Coolant Accidents, reactivity excursions, system failures, etc.
Severe Accident Management Guidelines (SAMG)
  To prevent releases when EOPs don’t work anymore
Firefighting
Damage control

## Slide 12: Taking urgent protective actions and other response actions
Urgent protective actions are meant to:
prevent severe deterministic effects
reduce the risk of stochastic effects (cancers)
prevent the public from doing more harm than good when protecting themselves

## Slide 13: Taking urgent protective actions and other response actions – cont’d
Two possibilities:
Before or shortly after the release based on EALs (upon declaration of a general emergency), according to the pre-developed protection strategy
After the release, based on OILs, through conducting monitoring and sampling programmes
  Arrangements must be made in the preparedness stage to effectively and safely take urgent protective actions
  Factors such as availability of transport and effectiveness of shelters and other local characteristics and infrastructure must be considered
Notes: There are two possibilities to initiate protective actions.
- They can be ordered within the predetermined emergency planning zones and distances upon declaration of General Emergency, therefore based on EALs.
- They can be ordered after the release as the result of monitoring and sampling, therefore based on OILs.
As the name of urgent protective actions itself suggests, there is an urgency and time constrain when they are to be implemented in order to be effective.
If the decision making and planning process for emergency response only begins when the emergency has already started, urgent protective actions may not be effectively taken and many lives may be in danger.
Therefore, arrangements must be made in the preparedness stage to effectively and safely take urgent protective actions when needed. Factors such as availability of transport and effectiveness of shelters and other local characteristics and infrastructure must be considered.

## Slide 14: Public protective actions
  Urgent protective actions
    Referred to as ‘precautionary urgent protective actions’ when taken on the basis of plant conditions, before or shortly after a release
  Early protective actions
Other response actions (which are not protective)
    Provision of public information
    Medical care
    Psychological support
Notes: There are two categories of protective actions for the public in response to severe nuclear emergency:
Urgent protective actions, and
Early protective actions.
These protective actions are usually accompanied with other response actions that aim to provide support to affected population through undertaking public information activities, provision of necessary medical care and psychological support and similar.
Sometimes the term precautionary urgent protective actions is used, which is not another category of protective actions, but just to point out that urgent protective actions are to be taken on the basis of plant conditions, before or shortly after a release.

## Slide 15: Urgent vs. early protective actions
Urgent protective actions
  To be taken promptly (within hours) to be effective
  Require prompt decision-making
  Are used over a relatively short period of time (days/weeks)
Early protective actions
  Can be implemented within days to weeks and they will still be effective
  They can be long lasting
Notes: Urgent protective actions are primarily intended to prevent deterministic effects. They must be taken promptly (within hours) to be effective and therefore require quick decision-making. They are used over a relatively short period of time (days/weeks).
While early protective actions are intended to reduce the risk of stochastic effects as far as reasonably possible. They can be implemented within days to weeks and they will still be effective. They can be long lasting.

## Slide 16: Urgent vs. early protective actions – cont’d
Major urgent protective actions:
Iodine thyroid blocking (ITB)
Evacuation
Sheltering
Major early protective action:
Relocation
Urgent and early:
Closing off the area
Preventing inadvertent ingestion
Personal decontamination
Restrictions on food, milk and drinking water and on commodities
Medical treatment
Notes: Some of protective actions are used only as urgent and one only as early, but there are more protective actions that can be used as both.
We have been briefly addressing them in Unit 1.

## Slide 17: Providing instructions and warnings to the public For whom?
Information should be provided to all groups:
Permanent population (residents)
Transient population (residing days to weeks)
Special population groups (disabilities, minors, elderly)
Special facilities
  Schools; Kindergartens; Hospitals; Retirement; Nursing homes; etc.
Notes: The information should be provided to all groups of population:
- The permanent population (residents),
- Transient population (people residing for a short period of time, days to weeks),
- Special population groups (people with disabilities, minors, and the elderly; Special populations often require special attention for physical, mental or emotional differences) and those responsible for them, and
- To special facilities within the emergency planning zones (schools, kindergartens, hospitals, retirement and nursing homes, prisons and such).

## Slide 18: Providing instructions and warnings to the public General rules:
Effective messaging may be critical to saving lives and minimize consequences
Messages should:
  Be timely and factual
  Contain clear, concise, reliable advice
All existing and still operational means should be used to convey messages to the affected people:
  TV, radio, sirens, e-mail alerts, text messaging, social media outlets

## Slide 19: Emergency warning systems
Have to be installed and maintained operational for warning and instructing the public within the EPZs:
    TV and radio emergency channels, sirens, e-mail alerts, text messaging, social media outlets (e.g. Facebook or Twitter)
  Have to be identified and used within territories for providing warnings and instructions to the public in case of a radiological emergency at unknown location
  Planners need to know what types of systems are available

## Slide 20: Protecting emergency workers and helpers
Emergency workers: Personnel having specified duties in an emergency, who might be exposed while taking actions
  Includes those employed by registrants and licensees
  Includes police officers, fire fighters, medical personnel and drivers and crews of evacuation vehicles
Emergency helpers: Members of
the public who willingly and
voluntarily help in response to a
nuclear or radiological emergency
Notes: In an emergency response, personnel from the facility, either employees who are directly employed or through a contractor, and also from response organizations such as fire fighters, police officers, medical personnel and drivers and crews of evacuation vehicles may be involved and have specific duties/tasks in support to mitigating the consequences of the emergency.
For example, some operating personnel supported by firefighters may be tasked with taking mitigatory actions to prevent conditions leading to core melt. Others, such as police officers, local and national rescue and monitoring teams may be engaged to implement public protective actions, such as evacuation, and to carry out monitoring activities.
They are all emergency workers and they need to be protected adequately.
Photo: The Fukushima emergency workers (© Reuters)

## Slide 21: Requirements for emergency workers
Should be clearly informed in advance of the associated health risks and protective actions
Should be trained
  In advance when pre-designated, or if not
  Just-in-time – before being assigned his/her task
Relevant requirements for occupational exposure in planned exposure situation are to be applied
No emergency worker should be subject to an exposure in an emergency in excess of 50 mSv
  Unless exceptional circumstances are present
Notes: IAEA Training in Emergency Preparedness and Response
21

## Slide 22: High doses on a voluntarily basis
Most response actions to be carried out within dose limits for occupational exposure
Critical actions (life saving, prevention of development of catastrophic conditions, averting large collective doses) may lead to incurring higher doses
They are to be taken on a voluntarily basis
  Subject to informed consent
To keep the doses of emergency workers as low as reasonable achievable
Notes: While most of the response actions may be carried out within dose limits for occupational exposure, many of the most critical actions may lead to incurring much higher doses, and as such, they are to be taken by emergency workers on a voluntarily basis. Such actions include:
- Lifesaving actions or actions for preventing serious injury,
- Actions to prevent severe deterministic effects,
- Actions to prevent development of catastrophic conditions that could significantly affect people and the environment, and
- Actions to avert a large collective dose.
All efforts need to be made to keep the doses of emergency workers as low as reasonable achievable, taking into account the guidance values discussed above. This imposes the need for managing and controlling the doses received by emergency workers and helpers in an emergency. Records must be kept in this regard.

## Slide 23: Restricting exposure of emergency workers and emergency helpers
Guidance values for restricting exposure of emergency workers are presented in Appendix I of GSR Part 7
Helpers in an emergency shall not be allowed to take actions that could result in doses > 50 mSv
Arrangements should be in place for:
  managing, controlling and recording the doses received
  appropriate specialized protective equipment and monitoring equipment
  medical follow-up and psychological counseling
  obtaining information to perform specified duties

## Slide 24: Managing medical response
Medical response is based on methods used for handling other types of accidents, with due consideration for:
    Health effects of radiation
    Contamination issues
Medical response needs to consider:
  Needs on-site: medical care for workers
  Needs off-site: medical care for workers and the affected population
Notes: Effective medical response is a necessary element of an overall response to nuclear emergencies. The basic principles of medical handling of exposed individuals are based, to a large degree, on the methods used for handling other types of accidents, taking into account the specifics of the possible health effects of radiation and problems with contamination.
Medical response in an emergency can be for workers on-site and for workers and population off-site. To organize the medical response, it is recommended that a system for medical support for nuclear emergencies is set up under the supervision of health authorities, e.g., Ministry for Health.

## Slide 25: Three levels of medical response
First aid on spot
Initial medical examination, treatment in a general hospital
Complete examination, treatment in a specialized medical centre
According to
  Degree of complexity
  Necessary resources for assistance
  Severity of consequences
Notes: The Ministry for Health is usually responsible for providing advice to other governmental offices on the health implications of any exposure to radiation. It is also responsible for ensuring that plans exist to provide treatment, monitoring and health advice to the public and to individuals, who have been contaminated or exposed to radiation, or those who fear they may have been.
In general, there are three levels of response, according to the degree of complexity, with respect to the necessary resources for support and the severity of consequences:
- First aid provided on spot,
- Initial medical examination and treatment in a general hospital, and
- Complete examination and treatment in a specialized medical centre for treatment of radiation injuries.

## Slide 26: Management of patients exposed to radiation
In case of high doses (deterministic effects)  Specialized medical hospital for complete medical examination, treatments, and assessment of the dose
In case of large number of exposed persons  Triage of persons: sorting patients on the basis of their condition to expedite clinical care and maximize use of available medical resources
Contaminated patients may require decontamination
  But decontamination should not delay the provision of critical medical care!
Notes: In case of serious injury, personnel from suitable medical centres should be available to respond and give first aid. In case of high doses, exceeding threshold for deterministic effects, immediate transport to specialized medical centre is recommended.
The IAEA has developed generic guidance on medical preparedness and response for nuclear or radiological emergencies.
For situations involving a large number of exposed people, e.g. evacuation during a release, one of the initial procedures is triage of people. These are actions to sort them into predetermined classes, on the basis of their injury or symptoms, to expedite treatment and maximize use of available resources.
The basic principle is that treatment of serious or life-threatening injuries must take priority over other actions.

## Slide 27: Communicating to the public during an emergency Challenge
Communicate in plain language
Public is very sensitive about anything nuclear
  all nuclear emergencies are perceived as dangerous  immense amount of media, public and political attention
Authorities to provide official information as soon as possible
  Even though not much information may be known at the time

## Slide 28: Effective public communications
Simplify the facts to avoid confusion and information overload
Build, maintain and increase public trust by being open and transparent
Coordinate messages and dissemination of information
Communication in a coordinated and consistent manner  speak with ‘one voice’
Assign spokesperson(s) and hold joint press conferences
Coordinate messages from different key stakeholders: operator, utility, regulatory body, local and national authorities
Notes: 28

## Slide 29: Involving the media
Identify key media in advance
Earn media trust
Exchange and maintain contact information
Prioritize media with most “reach” during an emergency
Proactive media relations in terms of interaction and frequency
“News servers” where media can get new information on topics they are interested in

## Slide 30: Emergency radiation monitoring
Monitoring purpose:
  To assess hazards
  To assess actions taken and to identify a need to adjust them
  To identify further actions to be taken
Decisions for protective actions based on OILs
Measurements may include:
  Ambient dose rate and dose
  Airborne radionuclide concentration
  Environmental deposition
  Food, water, and environmental contamination
  Individual dose
  Surface contamination measurements
Notes: Following a release from the reactor core or spent fuel pool decisions on protective actions are taken based on environmental measurements that can be obtained through field monitoring and sampling teams.
As soon as environmental measurements are available, monitoring data guide decision-makers to take protective actions on the basis of operational intervention levels (OILs).
After the implementation of urgent protective actions, the environmental monitoring data enables technical and decision-making staff to more accurately assess the level and degree of hazards, as well as its nature, extent and duration. Based on the monitoring data additional decisions on early protective and other response actions may need to be made or the ones in place adjusted.
The actual measurements to be made in an emergency may include:
- Ambient dose rate and dose,
- Airborne radionuclide concentration,
- Environmental deposition,
- Food, water, and environmental contamination,
- Individual dose, and
- Object-surface contamination measurements.
Measurements of airborne aerosols and gases are generally made to provide early warning of releases from unmonitored or as-yet unreported sources.
Environmental deposition measurements refer to the amount of radioactive material that has been deposited on ground or surfaces. These measurements are performed to characterize deposition, to determine the physical composition of deposition, to support dose calculations and protective actions’ decisions, and for public information purposes.
These measurements may also refer to the specific activity of soil, water, or plants. In this case, sampling of rain, run-off water, soil, grass, crops, etc., is required. Such results can be used to guide the initial food sampling efforts, for example, by concentrating in areas where the ground contamination exceeds pre-set limits.
When measuring food, water and environmental contamination, sampling and in many cases sample preparation is required. This is performed in fixed laboratories, although some measurements could be performed in mobile laboratories.

## Slide 31: Generic guidance on emergency monitoring
Phases | Type of measurements | Objectives
After declaration of General Emergency | Gamma/beta dose-rate measurements | To detect major release from the facility and to locate plume direction
During a release | Gamma/beta dose-rate measurements (from plume and ground deposition) Airborne radionuclide concentration measurements | To identify where gamma dose rates indicate urgent protective actions are warranted To determine radionuclide mix and measure radionuclide concentrations in air
After release has ended or after plume passage | Environmental deposition measurements Gamma dose measurements in the environment Food, water, and environmental contamination measurements Individual dose measurements | To implement protective actions To determine deposition maps for 131I and 137Cs and other important radionuclides To identify radionuclide mix in deposition To control personal exposure and contamination To determine food and drinking water contamination To assess doses to the public To plan follow-up actions and early protective actions
Notes: The table summarizes generic guidance on the type of radiation measurements during different phases of a nuclear emergency and what are objectives of such measurements.

## Slide 32: Managing radioactive waste
Radioactive waste is normal side product
  Ranges from spent nuclear fuel of NPPs (high level waste) to contaminated personal protective equipment (low level waste)
Major recovery and decontamination activities may be warranted in a nuclear emergency resulting in a large volumes of radioactive waste being produced
  Can easily overwhelm national capabilities for its management
Adequate preparedness to address waste management following the emergency is necessary
Notes: Radioactive waste is normal side product of regular activities involving nuclear or radioactive material. It ranges from spent nuclear fuel of NPPs (high level waste) to contaminated personal protective equipment (low level waste). Such waste and its management are under strict regulatory control, from cradle to grave (see Module 19 for more details).
During severe nuclear emergency radioactive material spreads into the environment contaminating individuals, fields, forests, roads, houses, playgrounds, cars, other surfaces etc. As a result, major recovery and decontamination activities may be warranted in order to protect people and the environment. These activities will inevitably result in radioactive waste that needs to be properly managed taking account of the fact that this is to be done in a manner that does not compromise the overall protection strategy.
The radioactive waste following a severe nuclear emergency may come in very large volumes that can easily overwhelm national capabilities for its management and thus, may require for new arrangements at the national level. Adequate preparedness need to account for the challenges and issues that can be faced in radioactive waste management following the emergency.

## Slide 33: International requirements on radioactive waste management
National policy and strategy for radioactive waste management
  applies for any radioactive waste, irrespective of its origin
Waste management following an emergency must not compromise the protection strategy
Preparedness requirements are essential and include:
  Waste characterization
  Criteria for waste categorization
  Waste minimization
  Methodology for predisposal and storage
  Dealing with human and animal remains

## Slide 34: Mitigating non-radiological consequences
Psychosocial, economic and other non-radiological consequences often outweigh radiological health effects
Difficult to mitigate - primary related to perceived risk
Measures to be considered
  Informing affected population accurately and promptly on accident’s progression, risks involved and protective actions being taken
  Keeping sheltered, evacuated, or relocated people informed of the expected time to return to normal
  Counselling and informing emergency workers and their families
Notes: The past emergencies demonstrated that psychosocial impacts, economic impacts and other non-radiological consequences often outweigh the actual radiation induced health effects. These consequences are to great extent associated with the perceived risk.
Both on and offsite emergency plans should explicitly recognize the significance of the psychosocial dimension and make provisions to reduce the detrimental effects it can create. Measures that should be considered include:
- Informing the affected population accurately and promptly of the emergency’s progression, the associated health hazards, and the protective actions being taken,
- Keeping sheltered, evacuated, or relocated people informed of the expected time at which they may return to normal activities and/or return to their homes,
- Ensuring that the public trusts the response organizations and is kept aware that measures are indeed being taken to protect them,
- Providing means to reassure people who believe that they themselves, their dwellings, and/or their properties may have been exposed or contaminated,
- Ensuring that goods coming from affected region are not contaminated to reassure the public,
- Counselling for emergency workers and their families.

## Slide 35: Terminating the emergency
Termination of an emergency and the subsequent transitioning shall be planned in the preparedness phase
Declaration of termination is end of transitioning and beginning of existing exposure situation (in severe nuclear accidents)

## Slide 36: Criteria for terminating the emergency
Qualitative and quantitative
Set-up during the preparedness phase
Adjusted during the response phase, according to the factual conditions
Based on a graded approach and considering national, local and site-specific circumstances

## Slide 37
2. Infrastructure elements for emergency preparedness and response

## Slide 38: What is needed to perform response functions
Authorities for EPR
Organization and staffing
Coordination
Plans and procedures
Logistical support and facilities
Training, drills and exercises
QM programme
Image courtesy IAEA

## Slide 39: Authorities for EPR
Established by means of acts, legal codes and/or statutes
Involvement of all response organizations
to be documented within the legislative
framework (e.g. emergency response plans)
Who is responsible for what?
  Facility, municipalities, regions, national
  For each organization, to be clearly addressed the authority and responsibility for: i) the direction and coordination of the response; ii) notification of other response organizations
  Conflicting roles and responsibilities need to be resolved
Arrangements for delegation and/or transfer of authorities to be described in relevant emergency plans

## Slide 40: Organization and staffing
Staff assignments based on qualification, their fitness and their intended duties
Organizational relationships and interfaces to be established
Positions responsible for preparedness activities to be assigned as part of the routine organizational structure
Organization for performing the response functions well established
Concept of operations and functional requirements taken into consideration
Staff considerations for long duration emergencies or for simultaneously managing more emergencies

## Slide 41: Block diagram – example:

## Slide 42: Coordination of emergency preparedness and response
Cooperation of several/many organizations
Some tasks require capabilities from more than one organization
  Example: food monitoring and control: ministries of agriculture, health, fisheries, environment, regulator
Agreements must be in place
  Working together, units, methods, transfer of information
Agreements in writing
  MoU, plans, others

## Slide 43: Incident Command System (ICS)
Is a standardized, on-scene, all-hazards incident management structure
Based on unified command and control concept
Allows for the integration of facilities, equipment, personnel, procedures and communications within a structure
Enables a coordinated response among various jurisdictions and functional agencies
Establishes common processes for planning and managing resources
Notes: Differentiate between:
Command: The act of directing, ordering, or controlling by virtue of explicit statutory, regulatory, or delegated authority.
Multiagency coordination: A process that allows all levels of government and all disciplines to work together more efficiently and effectively.
The organizational structure is important, but the process described by ICS is even more important.
ICS can be used during planned events (e.g., Major Public Events) or emergencies, but not during Recovery after an emergency is over.
An ICS is not:
A method to take away any agencies responsibilities
A method to change the chain of command within an agency
Always managed by the fire brigade
Too big or too small
Used just by government agencies and departments

## Slide 44: Coordination at national level
Coordinate planning and preparedness activities
Coordinate emergency arrangements:
  arrangements and protocols for operational interfaces
  arrangements to develop and harmonize tools, procedures or criteria for use in the response to nuclear or radiological emergency
  arrangements to harmonize radiation monitoring
  arrangements to harmonize assessments of contamination, doses and radiation induced health effects
Coordinate building infrastructure to support the response functions
Notes: For the Lecturer: details in relation to the importance and the mechanisms to achieve coordination of the emergency response will be provided in a separate lecture.

## Slide 45: Coordination at international level
  Arrangements and protocols with other States to
    Coordinate early notification, data and information exchange
    Public information
    Protective actions
  Special arrangements for States with areas in category V
    Early notification and information exchange
    Radiation monitoring
    Protective actions
Notes: Ref: GSR Part 7
The RB shall be the responsible organization to make arrangements on early notification and exchange of information for both preparedness and response phases of a nuclear emergency with those States that have areas in category V, so that the respective States are provided with appropriate information for developing their own preparedness to respond to a transboundary emergency and that appropriate coordination across national borders is in place. These arrangements shall include:
(a) agreements and protocols to provide information necessary to develop a coordinated means for notification, classification schemes and criteria for taking and adjusting protective actions and other response actions;
(b) arrangements for communication with the public;
(c) arrangements for the exchange of information between decision making authorities.
Same kind of arrangements and protocols shall be made by RB with neighbouring States, for the national areas in category V.
The RB shall make arrangements with other States for coordination of early notification, data and information exchange, public information and recommendations of protective actions and other response actions to co-national citizens and to embassies, in the event of a transnational emergency, in order either to ensure that they are consistent with those recommended in these States, or to provide an opportunity for them to explain to the public the basis for the differences.

## Slide 46: Plans and procedures
Emergency plans must be documented
  National, local and facility level
  Each organization
  Based on assessment of hazards
  Coordinated with other emergencies
Emergency plans must address all response functions and infrastructure requirements
  Must define: generic criteria, planning zones, classification system
  Must be implemented and periodically tested!

## Slide 47: Plans and procedures – cont’d
Procedures, analytical tools and computer programs must be developed
Procedures
  Common structure, appearance and terms
  Stand-alone
  Identify response position responsibilities
  Designed to respond to readily available information
  Must be tested under simulated conditions

## Slide 48: Logistical support and facilities
Needs analysis
Facilities for all response functions
Emergency tools, equipment and supplies
Laboratories for sample analysis
Survey and sampling teams
Information management
Communications systems

## Slide 49: Logistical Support and Facilities – cont’d
Locations and facilities must be
  Designed to support functions that will take place within them
  Usable under emergency conditions
  Integrated into ICS
Developing adequate facility or location
  Starts with determining functions of facility/location
  Ends with testing them (See Appendix 14 in EPR- Method)

## Slide 50: Logistical Support and Facilities – cont’d
Assembly point
Assistance centres
Control room
Designated hospital
Emergency operations facility
Facility medical service
Incident command post
Notification point
Operational support centre

## Slide 51: Logistical support and facilities – cont’d
Public information centre
Radiological monitoring and assessment centre
Referral hospital for over exposed/contaminated
Relocation/reception centres
Emergency operations centre
Staging area
Technical support centre
Triage area
Warning point

## Slide 52: Training, drills and exercises
Training requirements for each position
Training programme
Training material
Tests
Feedback process

## Slide 53: Systematic approach to training and exercises
Training and exercises programs to be designed and carried out systematically on the basis of:
  duties for all positions
  competences for all parties involved
System to track participation and outcomes
Exercises provide unique insight in the state of preparedness
  They are basis for continued improvement
  Need to be well organized, professionally conducted
  Their evaluation must focus on constructive improvement
53
Notes: Training and exercises to be effective they have to be carried out systematically.
It all starts with identifying of duties for all positions and competences for all parties involved.
According to these training and exercises can be designed, which are to be carried out through a continuous program.
Ideally a system is in place to track participation of individual team members in trainings and exercises, so that everyone receives the same amount of trainings on average corresponding to their duties.
Emergency response exercises can provide unique insight in the state of preparedness of emergency response organizations. They can also be the basis for continued improvement of emergency preparedness and response. However, to be most useful, emergency response exercise need to be well organized, professionally conducted and their evaluation must focus on constructive improvement potential. The IAEA EPR-Exercise publication provides comprehensive practical guidance on response exercises for emergencies involving all types of nuclear or radiological practices.
In general, nuclear facility such as power plants should hold one annual large-scale coordination exercise involving off-site authorities. The training and exercises should take into account the needs of the public living close to the facility as well.
53

## Slide 54: Quality management programme
Response organizations to establish comprehensive quality management programme that covers
  Availability and reliability of all supplies, equipment, communication systems and facilities
  Inventories, resupply, tests and calibrations
  Maintenance, review and updating of emergency plans, procedures and other arrangements
  Incorporation of lessons learned from research, operating experience and emergency drills and exercises
Sufficient resources be available to regularly test all the above
  Testing to be carried out systematically with a continuous program
54
Notes: The IAEA Safety Requirements for EPR require that the response organizations, including the operator, establish a comprehensive quality management program, covering:
- availability and reliability of all supplies, equipment, communication systems and facilities necessary to perform specified functions in an emergency,
- inventories, resupply, tests and calibrations
- maintenance, review and updating of emergency plans, procedures and other arrangements
- incorporation of lessons learned from research, operating experience (such as response to emergencies) and emergency drills and exercises.
In practice this means that procedures should be made and sufficient resources should be allocated to regularly test and/or review, as appropriate, all the above. Testing and reviewing, in order to be effective, have to be carried out systematically with a continuous program in place. Exercise and training programmes can be also used to serve this purpose too.
54

## Slide 55: Quality management programme – cont’d
Emergencies need to be
  Investigated and analysed and
  Necessary improvements identified and implemented
Lessons learned with international significance
  Reported to the IAEA
  IAEA reports and other reports of emergencies to be reviewed to identify relevant lessons
55
Notes: All significant emergencies and the response to them need to be carefully investigated, analyzed and the quality management system has to ensure that deficiencies are identified and corrective actions implemented.
Lessons learned that may have international significance should be reported to the IAEA, and vice versa, the IAEA reports and other reports of international emergencies should be reviewed to identify relevant lessons to be learned.
The internal and external auditing process must be established to regularly verify functioning of the quality management system.
55

## Slide 56: Emergency Preparedness Review - EPREV
Internal and external auditing process is necessary in order to regularly verify quality management system
IAEA offers to its Member States independent peer review of their emergency preparedness - EPREV
EPREV can cover all aspects
  From peer review of emergency arrangements at NPPs to full peer review of emergency arrangements within a State (at operator, local and national level)
56
Notes: In addition, IAEA offers to member states independent appraisal of their emergency preparedness and response arrangements, called EPREV – Emergency Preparedness Review. EPREV can cover all aspects, from the appraisal of the emergency arrangements at a specific installation to a full appraisal of all arrangements in a requesting member state, including on-site, off-site and national arrangements.
56

## Slide 57: Key points
Functional elements are related to the response functions which are to be performed in a nuclear or radiological emergency
  each organization to choose the functional elements applicable for their roles and responsibilities in an emergency
Infrastructural elements are to be established at the preparedness stage for effective implementation of the response functions in an emergency
International requirements in GSR Part 7 address all functional and infrastructural elements

## Slide 58: References
IAEA GSR Part 7
IAEA GSR Part 3
IAEA GS-G-2.1
IAEA EPR-Method 2003

## Slide 59
Thank you!
Notes: Thank you!

## Slide 60: Discussions on Unit 2 [10 minutes]
Notes: Thank you!