## Slide 1: Regulatory control
C.A. (Chuck) McDermott, P.Eng.
Canada
C_A_McDermott@icloud.com

## Slide 2: Contents
Overview of regulatory control
Legislative framework
Regulatory framework
Regulations and guides
Authorization
Review and assessment
Inspection
Enforcement

## Slide 3
Global nuclear safety and security framework

## Slide 5: Convention on Nuclear Safety
Entered into force on 24 October 1996
Currently has 84 Contracting Parties
Ghana became contracting party in August 2011
Incentive convention (encourages Contracting Parties to comply, but no provisions for sanctions if a Contracting Party does not)
First international legal instrument to explicitly consider nuclear safety
Notes: Before each course, update the number of contracting parties, available at the following website:
http://www.iaea.org/Publications/Documents/Conventions/nuclearsafety_status.pdf
If presenting at a national course, provide the date that the country became a contracting party (or state if the country is not a party)

## Slide 6: Elements of the national safety infrastructure
Legal framework
Regulatory body
Technical and industrial framework
Scientific and economic framework
Nuclear education and training

## Slide 7: Positioning the regulatory body
International Framework
Regional Networks
National infrastructure
Regulatory Body

## Slide 8
Overview of regulatory control

## Slide 9: Overview
Sound regulatory control is essential for ensuring that a nuclear power plant is safely:
  Sited;
  Designed;
  Constructed;
  Commissioned;
  Operated; and
  Decommissioned.

## Slide 10: Overview (Cont’d)
Regulatory body acts independently of authorized party in national interest to ensure that level of safety is appropriate.
However, this does not reduce the responsibility of authorized party to ensure that its activities are safe.

## Slide 11: Main functions of a regulatory body (RB)
Establishing requirements;
Issuing authorizations;
Reviewing and assessing submissions from applicants and authorized parties;
Inspecting facilities and activities;
Enforcing compliance; and,
Communicating with interested parties.

## Slide 12
Legislative framework

## Slide 13: Learning objectives
Describe the legislative framework that is necessary for regulatory control to be effective.
Describe a possible legal structure of a comprehensive nuclear law.

## Slide 14: Legislative framework
Achieving and maintaining a high level of safety in nuclear power plants (NPPs) depends on sound legislative framework
Legislative framework describes how State will control the use of nuclear energy and provide necessary mechanisms and resources for this control
IAEA Safety Standard GSR Part 1: Governmental, Legal and Regulatory Framework for Safety describes requirements for an adequate legislative framework
This course focuses on NPPs, although most concepts are applicable to all nuclear facilities and activities

## Slide 15: Prime responsibility for safety
First principle in IAEA Safety Fundamentals (SF-1) states:
  "The prime responsibility for safety must rest with the person or organization responsible for facilities and activities that give rise to radiation risks".
The operating organization (authorized party) has essential and central role and, therefore, bears an important responsibility.
Legislative framework must ensure that prime responsibility remains with authorized party.

## Slide 16: Legislative provisions
Legislation is how a State establishes control over use of nuclear energy
Legislation should:
  Set out objectives for protecting individuals, society and the environment;
  Articulate national policy and strategies for nuclear safety;
  Prohibit use of nuclear energy without authorization;
  Establish a RB with appropriate authority;
  Provide RB with adequate human and financial resources; and,
  Establish offences and corresponding penalties for contraventions.

## Slide 17: Legislative provisions (cont’d)
Legislation should give RB authority to:
  Define and develop policies, safety principles/requirements and associated criteria;
  Establish regulations and issue guidance;
  Issue, amend, suspend or revoke authorizations;
  Inspect for compliance
  Enforce its regulations
  Communicate and liaise directly with public, other interested parties, other RBs and international organizations

## Slide 18: Comprehensive nuclear law
One structure for a comprehensive nuclear law is illustrated below and on next four slides:
Parts | Article | Contents
PREAMBLE |  | 
OBJECTIVES | 1 | Objectives
DEFINITIONS | 2 | Definitions
SCOPE | 3 | Scope of application

## Slide 19: Comprehensive nuclear law (cont’d)
Parts | Article | Contents
REGULATORY BODY | 4 | Establishment of the regulatory body.
 | 5 | Functions and responsibilities.
 | 6 | Human and financial resources.
 | 7 | Advisory bodies.

## Slide 20: Comprehensive nuclear law (cont’d)
Parts | Article | Contents
AUTHORIZATION and NOTIFICATION | 8 - 11 | Authorizations
OPERATOR´S RESPONSIBILITIES | 12 - 13 | Responsibilities of authorized parties
INSPECTION and ENFORCEMENT | 14 - 15 | Inspection Enforcement

## Slide 21: Comprehensive nuclear law (cont’d)
Parts | Article | Contents
SPECIFIC PROVISIONS | Various | For each subject area, for example: Radiological Protection Radioactive material and radiation sources Safety of nuclear installations; Emergency preparedness and response; Mining and milling; Transport Radioactive waste and spent fuel;

## Slide 22: Comprehensive nuclear law (cont’d)
Parts | Article | Contents
SPECIFIC PROVISIONS (Cont’d) | Various | Nuclear liability and coverage; Safeguards; Export and import controls; and Physical protection
OFFENCES and PENALTIES |  | Offences. Penalties.
FINAL PROVISIONS | Various | Final clauses, for example: Amendments; Repeals of earlier laws; Transitional period; etc.

## Slide 23
Regulatory framework

## Slide 24: Learning objectives
Understand need for regulatory control
Describe role and organization of RB
Understand why independence is important for RB and how it can be achieved
Understand IAEA competency model for RBs
Identify core functions of RB

## Slide 25: Regulatory control
Most States prohibit use of nuclear energy except in accordance with an authorization by the RB
Authorizations are how State establishes and maintains regulatory control
Any authorization needs to ensure that prime responsibility for safety remains with authorized party

## Slide 26: Regulatory control (cont’d)
States use various terms for the concept of authorization, such as licence, permit or certificate.
IAEA (and this presentation) uses the terms authorization and authorized party.
An authorization is a formal permission issued to an authorized party, allowing the authorized party to site, construct, commission, operate or decommission a NPP.
Most authorizations include conditions that authorized party must comply with.

## Slide 27: Overlapping jurisdictions
In most States, RB is not the only authority that regulates some aspect of an NPP. Other authorities that may be involved include:
  Industrial health and safety authorities;
  Public health authorities;
  Environmental authorities;
  Building and electrical code authorities;
  Transport authorities (both for transport of dangerous good and for navigation purposes);
  Emergency preparedness and response authorities;
  Etc.

## Slide 28: Overlapping jurisdictions (cont’d)
To avoid conflicts, RB should establish formal agreements with other authorities to clearly define how they will operate in a coordinated manner to limit regulatory gaps and overlaps.
Even with formal agreements, good communication between various authorities is essential.

## Slide 29: The RB
RB is how the State exercises control over the safety of NPPs.
It includes:
  Sufficient competent technical staff
  Legal support
  Administrative support
Many RBs make use of advisory bodies of outside independent experts, but they are normally separate from RB.

## Slide 30: Organization of the RB
RB should be structured so it is capable of carrying out functions effectively, efficiently and independently
Appropriate structure of RB depends on many factors, including:
  Nature of the national legal infrastructure
  State’s cultural attitudes and traditions
  Existing governmental organization and procedures
  Technical, financial and human resources available in State
  Number and nature of regulated facilities and activities in State

## Slide 31: Organization of the RB (cont’d)
In some States, there is more than one responsible authority.
Typical situation is where one authority regulates radiation safety, while another regulates safety of facilities.
In these cases, government must establish arrangements that ensure regulatory responsibilities and functions are clearly defined and coordinated.

## Slide 32: Organization of the RB (cont’d)
If RB is not entirely self-sufficient in a technical or functional area, it should have the authority to seek advice or assistance from outside sources.
When such external advice or assistance is provided, arrangements should be made to ensure that those providing it are effectively independent.
Receiving external advice or assistance does not relieve RB of its responsibility for decision-making.

## Slide 33: Independence of the RB
An important attribute of RB is its freedom from unwarranted interference in its regulatory functions.
The Convention on Nuclear Safety states:
  “Each contracting party shall take the appropriate steps to ensure an effective separation between the functions of the RB and those of any other body or organization concerned with the promotion or utilization of nuclear energy.”
Even so, an independent RB will not be entirely separate from other governmental bodies.

## Slide 34: Independence of the RB (cont’d)
Measures that support effective independence include:
  Sufficient competent staff
  Sufficient financial resources
  Ability to make independent regulatory judgements and decisions
  Freedom from political and economic pressures
  Freedom from pressures from government departments, authorized parties, or other organizations
  Ability to give independent advice to government bodies on safety matters
  Access to the highest levels of government
  Ability to liaise with RBs of other States and with international organizations

## Slide 35: Management system of RB
RB must establish an integrated management system that meets requirements of IAEA Safety Standard GSR Part 2.
The module on Management Systems describes these requirements in detail and all are applicable to RB.

## Slide 36: Staffing and training for RB
Ability of RB to fulfil its responsibilities depends largely on competence of its staff.
IAEA Safety Standards and Safety Report No. 79 provide guidance on managing the competence of RBs.
Report 79 also provides guidance on delivering training and other elements of competence development.
  IAEA TECDOC 1757: “Methodology for the Systematic Assessment of Regulatory Competence Needs (SARCoN) for RBs of Nuclear Installations” also provides useful information.

## Slide 37: IAEA competence model
Competences comprise a combination of knowledge, skills and attitudes (KSAs).
KSAs for each position in RB need to be established.
IAEA competence model is based on a quadrant structure shown on next slide.

## Slide 38: IAEA competence model (cont’d)
1. Competences related to the legal, regulatory and organizational basis 1.1. Legal basis 1.2. Regulatory policies and approaches 1.3 Regulations and regulatory guides 1.4. Management system | 2. Technical discipline competences 2.1. Basic science and technology 2.2. Applied science and technology 2.3. Specialized science and technology
3. Competences related to the RB’s practices 3.1. Review and assessment 3.2. Authorization 3.3. Inspection 3.4. Enforcement 3.5. Development of regulations and guides | 4. Personal and behavioural competences 4.1. Analytical thinking and problem solving 4.2. Personal effectiveness and self-management 4.3. Communication 4.4. Team work 4.5. Managerial and leadership competences 4.6. Safety culture

## Slide 39: Core functions of the RB
The core functions of RB are:
  Establishing regulations and guidance;
  Issuing authorizations;
  Conducting reviews and assessments;
  Conducting inspections; and
  Taking enforcement actions.
We will talk about each of these in turn later.

## Slide 40: Core functions of the RB (cont’d)
Most RBs also consider provision of information as a core function.
RB should provide information to:
  Public;
  Media;
  Legislature; and
  Other interested parties.
There is a separate module on communication, so it will not be further discussed here.

## Slide 41: Additional duties of the RB
Every RB will have some role in emergency preparedness and response, but precise activities vary greatly among States.
RBs are responsible for ensuring that authorized parties have made adequate arrangements regarding emergency preparedness and response.
Most RBs also have a responsibility for advising the government on nuclear safety matters during emergencies.

## Slide 42: Additional duties of the RB (cont’d)
Specific to each State, but may include:
  Advising the government and other authorities on matters related to NPP safety;
  Confirming competence of personnel responsible for the safe operation of NPPs;
  Independent radiological monitoring in and around NPPs;
  Independent testing and quality control measurements;
  Initiating and coordinating safety-related research and development;
  Providing personnel monitoring services and conducting medical examinations;
  Monitoring of nuclear non-proliferation and implementing safeguards activities.

## Slide 43
Regulations and guidance

## Slide 44: Learning objectives
Identify IAEA guidance on regulations and guides
Describe purpose of regulations and guides

## Slide 45: IAEA guidance on regulations and guides
GSR Part 1 has three requirements on regulations and guides
Requirement 32:
  The RB shall establish or adopt regulations and guides to specify the principles, requirements and associated criteria for safety upon which its regulatory judgements, decisions and actions are based.
Requirement 33:
  Regulations and guides shall be reviewed and revised as necessary to keep them up to date, with due consideration of relevant international safety standards and technical standards and of relevant experience gained

## Slide 46: IAEA guidance on regulations and guides (cont’d)
Requirement 34:
  The RB shall notify interested parties and the public of the principles and associated criteria for safety established in its regulations and guides, and shall make its regulations and guides available.

## Slide 47: Regulations and guides
Regulations and guides provide the basis for other RB core functions and therefore should be in place early in nuclear power programme.
The IAEA Safety Requirements documents are written in a way that the RB can easily transform into regulations.

## Slide 48: Need for regulations and guidance
Regulations are mandatory requirements that authorized parties must comply with.
Guides provide advice on how applicants and authorized parties can meet the regulations.
Guides are not usually mandatory. Applicants and authorized parties are usually free to propose alternative ways of satisfying the Regulations.
States embarking on a nuclear power programme will already have some regulations and guides in place (radiation protection and possibly the authorization process).

## Slide 49: IAEA Standards for NPPs
Following IAEA Safety Standards provide sound basis for set of NPP regulations:
  GSR Part 2: Leadership and Management for Safety
  GSR Part 4: Safety Assessment for Facilities and Activities
  GSR Part 7: Preparedness and Response for a Nuclear or Radiological Emergency
  SSR 2/1: Safety of Nuclear Power Plants: Design
  SSR 2/2: Safety of Nuclear Power Plants: Commissioning and Operation

## Slide 50: IAEA Standards for NPPs (cont’d)
If a State does not already have regulations in place regarding radiation safety, GSR Part 3: Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards provides a basis for those regulations

## Slide 51: Exercise
Chapter 5 of SSR 2/1: Safety of Nuclear Power Plants addresses general plant design and includes five sections (shown on next slide)
Divide into five groups
Activity: For your assigned section
  Do current regulations in your country address the SSR 2/1 requirements?
  If yes, describe how you came to that conclusion.
  If no, draft a regulation that would address the SSR 2/1 requirements.

## Slide 52: Exercise (cont’d)
Group 1: Design basis
Group 2: Design for safe operation over the lifetime of the plant
Group 3: Human factors
Group 4: Other design considerations
Group 5: Safety analysis

## Slide 53
Authorization

## Slide 54: Learning objectives
Identify IAEA guidance on authorization
Describe authorization process
Understand requirements that applicant or authorized party must have in place for each stage of authorization process

## Slide 55: IAEA guidance on authorization
GSR Part 1 includes two requirements on authorization:
Requirement 23:
  Authorization by the RB, including specification of the conditions necessary for safety, shall be a prerequisite for all those facilities and activities that are not either explicitly exempted or approved by means of a notification
Requirement 24:
  The applicant shall be required to submit an adequate demonstration of safety in support of an application for the authorization of a facility or an activity

## Slide 56: Definitions
Authorization (licence, permit): A legal document issued by RB granting permission to create a NPP and to perform specified activities
Authorized party (licensee): Person or organization having overall responsibility for a NPP and possessing all necessary authorizations
Applicant: Person or organization who applies for authorization

## Slide 57: Prime responsibility for safety
Authorization must assign prime responsibility for safety to authorized party
Compliance with regulations and requirements imposed by RB does not relieve authorized party of its prime responsibility for safety
Applicant/authorized party must demonstrate to the satisfaction of the RB that this prime responsibility has been and will continue to be fulfilled

## Slide 58: Authorization principles
Authorization process should:
  Ensure important safety issues are dealt with properly
  Be understood by concerned parties
  Be predictable (well defined, clear, transparent and traceable)
  Be systematic
  Include discrete steps
  Follow a logical order
  Minimize duplication
  Provide clear division of responsibilities
  Give the public opportunities for early participation

## Slide 59: Duration of authorization
Authorizations may be granted:
  For a specific time period (e.g. 10 years, 40 years)
  for a specific stage in the lifetime of the nuclear installation
  For an indefinite period of time (a permanent authorization)
  For a specific activity

## Slide 60: Basis for authorization
Authorization establishes regulatory control over NPP
Relates State’s legal and regulatory framework to duties of authorized party
Involves fulfilment of regulatory requirements
Requires formal submissions by applicant
May also include agreements and commitments made between RB and applicant
Documents submitted in support of application are part of basis for authorization

## Slide 61: Considerations for authorization
Authorization should only be given when RB has confirmed that NPP is going to be used or conducted in a manner that does not pose an undue risk to workers, the public or the environment
Requires confirmation that applicant can fulfil its safety obligations
Authorization should be based on predefined documents that applicant submitted to RB
These documents should be reviewed by RB and should be updated regularly by authorized party

## Slide 62: Considerations for authorization (cont’d)
A clear and explicit set of requirements, criteria and standards forming the basis for authorization should be defined by regulation and by RB
A graded approach should be taken by RB when performing reviews, assessments or inspections
Applicant and RB should take into account international good practices
Analysis approach to safety should include deterministic and probabilistic methodologies and analytical tools
Integration of safety and security should be addressed

## Slide 63: Role of the RB
Publish requirements for application for authorization
Conduct reviews and assessments of applications and other submissions
Make regulatory decisions and to grant, amend, suspend or revoke authorizations
Conduct early assessment of competence and capability of applicant
Establish formal management system for dealing with applications

## Slide 64: Role of the RB (cont’d)
Set out arrangements for requesting further information from applicant
Inform applicant of decision
Record and keep documentation relevant to issuing of authorization

## Slide 65: Role of the RB (cont’d)
RB may request reassessment of safety in light of:
  Operating experience
  Information from research and development programmes and new knowledge of technical matters
  Changes in regulatory requirements
  Changes in the site conditions

## Slide 66: Role of the applicant
Prepare and submit a comprehensive application to RB that demonstrates that priority is given to safety
Meet its responsibility for safety at NPP
Understand design basis and safety analyses for NPP, and limits and conditions under which it must be operated
Exercise control over contractors
Implement process for modifications
Have design capability and effective external relationship with original designer

## Slide 67: Role of the applicant (cont’d)
Assess safety in a systematic manner and on a regular basis.
Maintain adequate human and financial resources
Implement procedures for:
  Controlling NPP within specified limits
  Managing anticipated operational occurrences and accident conditions
  Responding to a nuclear or radiological emergency
Periodically assess, review and revise procedures

## Slide 68: Main contents of an authorization
Unique authorization identification
Issuing authority
Identification of authorized party
Description of the NPP
Maximum allowable inventories of nuclear material
Requirements for notifying RB of any modifications that are significant to safety
Obligations of authorized party regarding safety

## Slide 69: Main contents of an authorization (cont’d)
Any limits on operation (e.g. power levels, dose limits, discharge limits, action levels, duration of authorization)
Requirements for reporting to RB:
  events and incidents
  routine reports
Requirements for retention of records
Requirements for arrangements for emergency preparedness
Documents which form basis for issuing the authorization

## Slide 70: Conditions of the authorization
Authorization should also include conditions, which are specific to the NPP
Can be groups into categories:
  Conditions that set technical limits and thresholds
  Conditions that specify procedures and modes of operation
  Conditions pertaining to administrative matters
  Conditions relating to inspection and enforcement
  Conditions pertaining to the response to abnormal circumstances
In many cases, conditions will reference authorized party documents

## Slide 71: Public participation
Public should be given opportunity to present views during certain steps of authorization process
This reinforces RB credibility and enhances public confidence in nuclear regulatory regime
Process should allow for challenging the issuing of an authorization on health and safety grounds
Public participation should continue throughout the lifetime of NPP
More information on public information in another module

## Slide 72: Graded approach
Resources devoted to authorization must be commensurate with magnitude of radiation risks
Application of graded approach by RB focuses how NPP is assessed, without unduly limiting authorized party and NPP operation
RB should use graded approach to determine scope, extent and level of detail of and effort to be devoted to authorization
Efforts should focus on aspects which involve untested (innovative) features

## Slide 73: Factors affecting graded approach
Account should be taken of:
  occupational doses
  radioactive discharges
  generation of radioactive waste
  potential consequences of anticipated operational occurrences and accidents
  possibility of occurrence of very low probability events with potentially high consequences
  maturity of applicant / authorized party organization
  use of proven designs, practices and procedures
  operating experience at similar NPPs

## Slide 74: Factors affecting graded approach (cont’d)
  uncertainties in performance of the NPP
  availability of competent staff and experienced managers, contractors and suppliers
  extent and difficulty of effort required to construct, maintain, operate and decommission
  number of related processes
  reliability and complexity of SSCs and their accessibility for maintenance, inspection, testing and repair.
Application of graded approach should be reassessed throughout authorization process. Adjustments may be made as better understanding of risks is obtained

## Slide 75: Site authorization
Before granting authorization for siting, RB should be satisfied that:
  Applicant is competent and capable
  Site characteristics are acceptable
  Baseline radiological survey is complete
  Basic design of NPP will meet safety requirements
  Applicant has adequate management system
  Research and development plans are adequate
  Arrangements for decommissioning and management of radioactive waste are adequate

## Slide 76: Authorization for construction
Before granting authorization for construction, RB should be satisfied that:
  Applicant’s management system (including provisions for control of suppliers and contractors) is adequate and functioning
  Site evaluation is acceptable
  Basic design is acceptable
  Preliminary Safety Analysis Report (PSAR) and its results are acceptable
  Financial arrangements (including for decommissioning) are acceptable
  Schedule for construction and acquisition of SSCs is adequate
  Industrial health and safety rules are in place

## Slide 77: Authorization for construction (cont’d)
Authorization for construction normally includes conditions regarding hold-points and requirements for further approvals by the RB, such as:
  Pouring of concrete
  Installation of certain components
  Authorizing nuclear or radioactive material on-site

## Slide 78: Authorization for commissioning
Normally a limited authorization for operation
Some overlap with construction
Issued in stages with hold-points
Demonstration that SSCs will perform as expected, both individually and in an integrated manner

## Slide 79: Authorization for commissioning (cont’d)
Before granting authorization for commissioning, RB should be satisfied that:
  commissioning test programme is complete and contains a set of well-defined operational limits, test acceptance criteria, conditions and procedures;
  commissioning tests can be safely conducted
  Management system is adequate
  Organizational structure of applicant is adequate
  Final Safety Analysis Report (FSAR) and its results are acceptable
  Arrangements for periodic testing, maintenance and inspection are adequate
  Process for change control is adequate

## Slide 80: Authorization of fuel loading
Before authorizing loading of nuclear fuel, RB must be satisfied that:
  As-built is reconciled against design
  Results of non-nuclear commissioning tests are acceptable
  Provisions for radiological protection are in place
  Operating instructions and procedures, especially operating procedures and emergency operating procedures are adequate
  Recording and reporting systems are in place

## Slide 81: Authorization of fuel loading (cont’d)
Before authorizing loading of nuclear fuel, RB must be satisfied that (cont’d):
  Arrangements for training and qualification of NPP personnel, including staffing levels and fitness for duty are adequate
  Authorized party management system is adequate
  On-site and off-site emergency preparedness are in place
  Accounting measures for nuclear and radioactive materials are in place
  Physical protection is adequate
  Arrangements for periodic testing, maintenance, inspection, control of modifications and surveillance are in place

## Slide 82: Authorization of routine operation
Before authorizing routine NPP operation at full power, the RB must be satisfied that:
  Results of commissioning tests are acceptable
  Limits and conditions for operation are in place
  FSAR has been updated

## Slide 83: Discussion
One of the considerations is that of public involvement.
What ideas do you have on how the RB can meaningfully involve the public in its authorization activities?

## Slide 84
Review and assessment

## Slide 85: Learning objectives
Identify the IAEA guidance on review and assessment
Describe the purpose of review and assessment by the RB
Describe the general steps in review and assessment
Understand the concept of defence in depth

## Slide 86: IAEA guidance on review and assessment
GSR Part 1 includes two requirements on review and assessment:
Requirement 25:
  The RB shall review and assess relevant information… to determine whether facilities and activities comply with regulatory requirements and the conditions specified in the authorization. This review and assessment… shall be performed prior to authorization and again over the lifetime of the facility….
Requirement 26:
  Review and assessment of a facility or an activity shall be commensurate with the radiation risks associated with the facility or activity, in accordance with a graded approach

## Slide 87: Objective of review and assessment
Overall objective is to determine whether the applicant’s submissions demonstrate that NPP complies with regulatory requirements
Confirmation that:
  Available information demonstrates the safety of the NPP
  Information contained in submissions is accurate and sufficient
  Technical solutions, and in particular any novel ones, have been proven or qualified by experience or testing or both, and are capable of achieving the required level of safety

## Slide 88: Management of review and assessment
Review and assessment for an NPP requires considerable effort
Consideration should be given to assigning managerial responsibility to a single individual or organizational unit
The RB will need to cooperate with the applicant to ensure review and assessment is effective and informed
Information from other sources (such as incident reports from other States) which have a bearing on the safety of the NPP should also be reviewed and assessed

## Slide 89: Management of review and assessment (cont’d)
Management of review and assessment should include responsibility for:
  Planning and directing the process
  Preparing procedures
  Coordinating information exchange between RB and applicant
  Log and follow-up all documents sent or received
  Monitoring status of submissions and reviews and assessments against schedule
  Making arrangements for various parts of RB to combine expertise

## Slide 90: Management of review and assessment (cont’d)
The management of review and assessment should include responsibility for (cont’d):
  Making arrangements for coordination between activities
  Making arrangements for liaison with consultants, advisory committees or other organizations
  Facilitating consultation with other RBs and government departments
  Collating and disseminating overall findings
  Planning for public consultation
  Planning for any hearing process
  Qualification and training of RB personnel

## Slide 91: Scheduling of submissions
RB should advise applicant of the period of time that it will take for the review and assessment
RB and applicant should reach agreement on schedule
RB needs to recognize that information initially submitted may be incomplete
Important issues will arise, necessitating additional studies and extending the time necessary for RB review and assessment
RB should make best effort to comply with schedule, but must not compromise its responsibilities

## Slide 92: Use of consultants
RB must have sufficient competent staff to conduct review and assessment
Even so, in some cases the RB may not have all the specialized technical knowledge required and will need to engage consultants
RB should have competent staff to oversee and evaluate the work of consultants
Use of consultants does not relieve RB its responsibilities

## Slide 93: Relationship between RB and applicant
Formal communication between applicant and RB should be established
Informal communications among specialists to clarify issues should be encouraged, but requests for additional work must go through formal channels
Where an applicant’s contractor has needed information, applicant must make necessary arrangements. This may include direct contact between RB and contractor
These contacts must not diminish applicant’s responsibility

## Slide 94: Relationship with RBs of other States and international organizations
Particularly useful where other RBs have experience in authorizing similar facilities
Specific reasons include:
  Gaining knowledge of authorization basis
  Gaining knowledge of a novel facility
  Adding to database of operating experience
  Gaining knowledge of different methods of analysis, such as methods using computer codes
  Gaining knowledge of applicant’s contractors
  Obtaining information on facilities in other States which may have an influence on safety

## Slide 95: Review and assessment plan
Perform an acceptance review. Submissions that are deficient are returned to applicant for correction
Define scope of review and assessment
Specify acceptance criteria
Identify additional information needed
Perform a step by step review and assessment procedure to determine whether the acceptance criteria are met
Decide on acceptability of applicant’s submission

## Slide 96: Scope and depth of review and assessment
Depends on several factors, including:
  Novelty
  Complexity
  Previous experience
Major feature is analysis of normal and fault conditions
Is not a repetition of work done by applicant
Rather, it is work done to confirm that applicant’s submissions are accurate and sufficient

## Slide 97: Bases for decisions
Factors that should be taken into account include:
  Extent to which safety objectives and regulatory requirements are met
  Depth and detail of submission
  Current state of knowledge
  Confidence in the conclusions
RB will not have, in advance, requirements covering all areas subject to review and assessment. RB will need to evaluate acceptability of applicant’s proposals on a case-by-case basis using general principles
Be careful when using industry standards for components

## Slide 98: Reference (generic) submissions
Definitions:
  Reference NPP: A designated existing NPP who’s design will be copied in other locations
  Generic NPP: A NPP design that will be constructed with relatively minor modifications in various locations
Reference or generic submissions may be appropriate where applicant will make multiple submissions
RB should apply same rigour in its review as for other submissions

## Slide 99: Reference (generic) submissions (cont’d)
RB cannot grant authorization based solely on reference or generic submission since safety depends on siting related, managerial and operational aspects
RB authorization should be limited to generic design
For a specific NPP, the applicant would then only need a submission concentrated on where the proposed NPP differs from reference or generic NPP

## Slide 100: NPPs already authorized in another State
RB must still perform independent review and assessment
RB may take into account other State’s RB review and assessment
RB should establish close contact with other State’s RB to facilitate review and assessment

## Slide 101: Audit calculations
RB may perform limited number of audit calculations
Reasons include:
  Identifying weaknesses, if any, in safety case
  Estimating safety margins or degree of conservatism
  Performing sensitivity analyses and uncertainty analyses to verify applicant’s designation of risk significance of various SSCs
  Verifying that safety assessment is consistent with current data
  Gaining further confidence in its own decision-making process
  Developing in-house capacity
Not cost effective nor appropriate for RB to redo entire set of calculations

## Slide 102: Defence in depth
A combination of a number of consecutive and independent levels of protection that would have to fail before harmful effects could be caused to people or to the environment.
Objectives of defence in depth:
  to compensate for potential human and component failures
  to maintain effectiveness of barriers by averting damage to NPP and to barriers themselves
  to protect public, workers and environment from harm if barriers are not fully effective

## Slide 103: Defence in depth
Five levels of defence in depth:
  Level 1: Prevention of abnormal operation and failures
  Level 2: Control of abnormal operation and detection of failures
  Level 3: Control of accidents within the design basis
  Level 4: Control of severe conditions, including prevention of accident progression and mitigation of the consequences of a severe accident
  Level 5: Mitigation of the radiological consequences of significant external releases of radioactive material

## Slide 104
Inspection

## Slide 105: Learning objectives
Identify the IAEA guidance on inspections
Describe the types of inspections that RB should perform
Describe the general steps in preparing for an inspection
Describe the basic elements of an inspector training and qualification programme

## Slide 106: IAEA guidance on inspection
GSR Part 1 includes three requirements on inspection:
Requirement 27:
  The RB shall carry out inspections of facilities and activities to verify that the authorized party is in compliance with the regulatory requirements and with the conditions specified in the authorization
Requirement 28:
  Inspections of facilities and activities shall include programmed inspections and reactive inspections, both announced and unannounced

## Slide 107: IAEA guidance on inspection (cont’d)
Requirement 29:
  Inspections of facilities and activities shall be commensurate with the radiation risks associated with the facility or activity, in accordance with a graded approach

## Slide 108: General aspects of inspection
The primary purpose of regulatory inspections is to independently provide a high level of assurance that activities performed at the NPP comply with regulations and conditions of authorization.
Inspection by the RB must not diminish the prime responsibility for safety of the authorized party
Inspection by the RB is not a substitute for control, supervision and verification activities by the authorized party
Inspection is unlike other regulatory activities in that it is not conducted at the RB’s offices

## Slide 109: Graded approach to inspection
The RB inspection programme will only inspect a small sample of the authorized body’s activities
The RB should use a graded approach to select those authorized party programmes, activities and facilities that are risk significant for inspection
The RB can use insights from its review and assessment activities to determine the risk significance

## Slide 110: Types of inspections
Inspections can be classified in three ways:
  Programmed or reactive
  Announced or unannounced
  Individual inspector or team inspection

## Slide 111: Programmed inspections
The need for and scope of these inspections is determined as part of the RB’s planning cycle
The inspection programme should include a sample of many different activities and structures, systems and components (SSCs) in the NPP
Some authorized party activities, programmes or SSCs will be inspected more than once a year, while others may only be inspected annually, every two years, every five years or once in an authorization period

## Slide 112: Reactive inspections
Inspections that are not identified during the RB planning cycle
Usually the result of operating experience or an abnormal occurrence
Requires the RB to have some flexibility
Although the scope of reactive inspections cannot be known during the planning cycle, the RB should allocate some resources (inspector, financial, time) for reactive inspections
The authorized party must investigate all abnormal occurrences, regardless of whether the RB is conducting a reactive inspection

## Slide 113: Announced inspections
The RB gives the authorized party notice of the inspection
The inspector can obtain required documentation in advance.
The inspector can schedule the inspection to ensure that:
  Activities the inspector needs to see will take place
  Equipment the inspector needs to see is available
  Personnel the inspector needs to interview are available
However:
  The authorized party has the opportunity to correct deficiencies or non-compliances
  The inspector may not get an accurate view of typical authorized party behaviour

## Slide 114: Unannounced inspections
An unannounced inspection allows the inspector to see the facility or activity as is. The authorized party does not have time to correct deficiencies or non-compliances.
For RBs with resident inspectors, most of the resident inspector inspections can be unannounced.
However:
  Key personnel may not be available;
  The part of the facility that the inspector wants to inspect may not be accessible
  The authorized party may not be performing the activity that the inspector wants to inspect

## Slide 115: Preparation for an inspection
Regardless of the type of inspection, preparation is essential.
In all cases, preparation should include:
  Confirmation of the scope of the inspection
  Review of the applicable regulations or conditions of authorization
  Review of previous inspection reports and enforcement actions
  Review of correspondence between the RB and the authorized party
  Review of authorized party documentation

## Slide 116: Data gathering techniques
Review of documents
Observation of SSC or activity
Interviews
Tests and measurements

## Slide 117: Review of documents
In many cases, this can (and should) be done before arriving at the NPP
Some examples include:
  Authorized party inspection reports
  Operating logs
  Modification and maintenance records
  Training records
  Radiation survey results
  Procedures

## Slide 118: Direct observation
A reliable method for inspection
Things to observe:
  Equipment condition (serviceability, availability, leaks, valve line-up, etc.)
  System parameters (temperatures, pressures, levels, flows, etc.)
  Activities (shift turnover, safety system testing, operator routines, maintenance activities, construction activities, emergency drills, etc.)
For equipment, take pictures if possible
Do not touch, do not interfere
Introduce yourself when observing activities

## Slide 119: Interviews
Useful for obtaining background information
Interview a cross-section of staff (operators, mechanics, technicians, supervisors, specialists, managers)
Prepare questions in advance
  Open-ended (questions that start with “please describe” “please explain”)
Interview in a location that will put person at ease (private but close to their workplace)
Listen and do not interrupt
Think about how you will validate what you were told

## Slide 120: Tests and measurements
Limited opportunities in operating NPPs:
  Radiation surveys
  Environmental sampling
For construction, if the authorized party is taking samples of concrete or metals, you could ask for a sample and subject it to independent testing
Never touch anything without explicit authorized party approval
Never remove anything from NPP without telling authorized party

## Slide 121: Inspector behaviour
For the vast majority of authorized party staff, inspectors are the only interaction with the RB
Know, understand and follow all RB processes and procedures regarding inspection
Be prepared
Be professional at all times
Treat authorized party staff with respect

## Slide 122: Inspector behaviour (cont’d)
Follow all authorized party rules unless they conflict with RB rules
Recognize that authorized party staff will have more knowledge and skill in NPP construction or operation than you
Adopt a “no surprises” approach: let someone know if you see something wrong
Take notes
Do not act as a consultant for the authorized party

## Slide 123: Inspection reports
The RB should establish a standard format for inspection reports
The inspection report should be completed as soon as possible following the completion of the inspection.
In many cases, the inspector may be able to provide a copy of the inspection report at the close of the inspection
Inspection reports should feedback into the regulatory process

## Slide 124: Training and qualification of inspectors
Training and qualification of inspectors requires substantial effort from the RB
Not possible to obtain an “inspector’s designation” from a university, college or other organization
In addition to technical training on NPPs, inspectors need training in inspection techniques, communication skills, legal aspects, etc.
On-the-job training, under the supervision of an experienced inspector, is a common training method
Experience shows that training and qualification of an inspector will take between 18 and 24 months

## Slide 125: Exercise
In two months time, the authorized party will begin pouring the base mat for the reactor building at your new NPP.
You have just been assigned responsibility for leading a team of four conducting an inspection of this activity
In groups of 4, complete the following:
  Describe the major activities you will do to prepare for the inspection
  Describe the expertise that the team should have
  Describe where will you find the regulatory requirements for the inspection

## Slide 126
Enforcement

## Slide 127: Learning objectives
Identify IAEA guidance on enforcement
Describe enforcement options for a RB
Describe the factors a RB should consider regarding enforcement

## Slide 128: IAEA guidance on enforcement
GSR Part 1 includes two requirements on enforcement:
Requirement 30
  The RB shall establish and implement an enforcement policy within the legal framework for responding to non-compliances by authorized parties with regulatory requirements or with any conditions specified in the authorization
Requirement 31
  In the event that risks are identified, including risks unforeseen in the authorization process, the RB shall require corrective actions to be taken by authorized parties

## Slide 129: Enforcement
RB must have authority to enforce regulatory requirements.
Goal of any enforcement action is to return the authorized party to compliance.
In fulfilling its statutory obligations, the RB must ensure that corrective actions are taken if unsafe or potentially unsafe conditions are detected.

## Slide 130: Enforcement (cont’d)
Enforcement actions must:
  Respond to the non-compliance; and
  Be commensurate with the seriousness of the non-compliance.
Thus, there is a range of different enforcement actions, from written warnings to penalties and, ultimately, withdrawal of an authorization.
In all cases, the authorized party is required to:
  Remedy the non-compliance;
  Perform an investigation, and
  Take all necessary measures to prevent recurrence.

## Slide 131: Factors to be considered for enforcement
The safety significance of the deficiency;
The complexity of the corrective action needed;
The seriousness of the violation;
Whether it was a repeat violation;
Whether it was a wilful violation;
Who noted and reported the non-conformance;
The past performance of the authorized party; and
The need for consistency in the treatment of authorized parties.

## Slide 132: Written warnings or directives
The most common form of enforcement action
In the case of NPPs, usually sufficient to remedy the safety issue
Should identify:
  The nature and basis of the violation
  The period of time permitted for taking remedial action
  Any compensatory measures to be taken (if any) until remedial action is complete

## Slide 133: Orders to curtail specific activities
If there is:
  Evidence of a deterioration in the level of safety; or
  In the event of serious violations which in the judgement of the RB pose an imminent radiological hazard to workers, the public or the environment,
the RB must require the authorized party to:
  Curtail activities; and
  To take any further action necessary to restore an adequate level of safety.

## Slide 134: Modifying, suspending or revoking an authorization
For NPPs, modifying the authorization (usually by requiring the reactor to be and remain shutdown) is preferable:
  Keeps authorized party under regulatory control
  All conditions of authorization remain in effect
Used in the event of a continuing or serious non-compliance that poses an immediate threat to the health and safety of persons or the environment

## Slide 135: Penalties
The RB should have the authority to:
  Impose or recommend penalties, for example, fines on the authorized party; and/or
  Institute or recommend prosecution through the State legal system
The use of penalties is usually reserved for serious or repeated violations, or for wilful non-compliance.

## Slide 136: Appeal of enforcement actions
Authorized party should be able seek a review of enforcement action, either through:
  An independent judicial body; or
  A government appeals process
Authorized party must comply with enforcement action while review is underway

## Slide 137: Inspectors and enforcement
Authority of inspectors to take on-the-spot enforcement action varies from State to State.
Where an individual inspector does not have authority to take on-the-spot action, measures must be in place to ensure that timely action will be taken.
For NPPs, situations that require inspectors to take immediate on-the-spot enforcement action are rare.

## Slide 138: Enforcement process
In most cases, implementing corrective actions will take time. Time allowed, and whether compensatory measures should be put in place in the meantime, will depend on increase to risk posed by deficiency.
Once authorized party has completed corrective actions, RB should consider conducting a follow-up inspection to confirm that corrective actions are effective.
RB should keep records of decisions relating to enforcement actions.

## Slide 139: Exercise
For the situations on the following two slides:
Determine whether there is a non-compliance
For the non-compliances:
  rank them from most to least serious
  Determine the appropriate enforcement action

## Slide 140: Exercise (cont’d)
You review 20 work orders, all of which should have been signed by the maintenance manager. Two of the work orders were not signed
A counterfeit component was knowingly installed in a safety system. The authorized party took great effort to conceal this, but you found it anyway
Last year, three workers at the NPP exceeded the annual dose limit for occupationally exposed workers

## Slide 141: Exercise (cont’d)
During a plant tour, a high school student received a whole body dose of 0.1 mSv
Authorized party procedures (not referenced in the authorization) require that operating documents be reviewed every three years. The authorized party conducted an audit and determined that only 75% of operating documents had been reviewed in the previous three years.
The specification for rebar in the concrete of the base mat called for 2 cm rebar with 0.5 m spacing. After pouring, it was determined that 1.5 cm rebar at 0.45 m spacing was used.

## Slide 142
Summary

## Slide 143: Summary
Overview of regulatory control
Legislative framework
Regulatory framework
Regulations and guides
Authorization
Review and assessment
Inspection
Enforcement

## Slide 144: Key points
  The prime responsibility for safety must rest with the authorized party
Role of RB is to ensure that authorized party takes its responsibility seriously
Core functions of the RB
  Regulations and guides
  Authorization
  Review and assessment
  Inspection
  Enforcement

## Slide 145: List of abbreviations
FSAR final safety analysis report
KSA knowledge, skills and attitudes
NPP nuclear power plant
PSAR preliminary safety analysis report
RB regulatory body
SSCs structures, systems and components

## Slide 146: References
SF-1: Fundamental Safety Principles
GSR Part 1: Governmental, Legal and Regulatory Framework for Safety
GSR Part 2: Leadership and Management for Safety
GSR Part 3: Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards
GSR Part 4: Safety Assessment for Facilities and Activities

## Slide 147: References
GSR Part 7: Preparedness and Response for a Nuclear or Radiological Emergency
SSR 2/1: Safety of Nuclear Power Plants: Design
SSR 2/2: Safety of Nuclear Power Plants: Commissioning and Operation
GS-G-1.1: Organization and Staffing of the Regulatory Body for Nuclear Facilities
GS-G-1.2: Review and Assessment of Nuclear Facilities by the Regulatory Body

## Slide 148: References
GS-G-1.3: Regulatory Inspection of Nuclear Facilities and Enforcement by the Regulatory Body
GSG-4: Use of External Experts by the Regulatory Body
SSG-12: Licensing Process for Nuclear Installations
SSG-16: Establishing the Safety Infrastructure for a Nuclear Power Programme
Safety Report No. 79
  IAEA TECDOC 1757: Methodology for the Systematic Assessment of Regulatory Competence Needs (SARCoN) for Regulatory Bodies of Nuclear Installations

## Slide 149: Use this box for any additional message
Thank you!
Notes: Thank you!